## Slide 1: Cable Design Project
Charity Fischer

## Slide 2: The Project
To design a cable for a 60 ton vehicle, cable must:
  Be 25 feet long
  Have no more than 10% elastic deformation
Examine 4 different materials
Calculate thermal expansion
Conduct fatigue analysis
Analyze 14 different diameters between 2 and 1/64 inches
Notes: The project was to design a cable for a 60 ton vehicle that had to be 25 feet long and could have no higher that 10% elastic deformation. I analyzed 4 different materials in the course of this project. I calculated the thermal expansion and I did a fatigue analysis. The project was mostly to choose between 4 different materials and 14 different possible diameters for the cable. Those diameters ranging from 2 inches to 1/64th of an inch.

## Slide 3: Introduction
4 materials examined:
  2014-T6 Aluminum, 1045 Steel, Copper, Titanium Ti-6AI-4V (Grade 5), Annealed
Thermal expansion analysis using change in temperature to find change in length
  Change in temperature was in 20 degree increments from 0 to 300
Fatigue analysis on Aluminum and Steel
Excel was used for calculations
Notes: During the course of this project I analyzed 4 materials; aluminum, steel, copper, and titanium as candidates for the cable.
I found the thermal expansion of each material by using change in temperature to find the change in length. The temperatures I used were 0, 20, 40… etcetera up to a change of 300 degrees all in Fahrenheit. I did a fatigue analysis on aluminum and steel using the S-N curves. And all my calculations were done using Excel.

## Slide 4: The Results
Stress found with σ=2P/πdt
Then put into the S-N curves to find number of cycles for Aluminum and Steel
Steel: 10^9
Aluminum: 10^8
Notes: By using the calculated stress for my chosen diameters I calculated how many numbers of cycles each of my materials would get.

## Slide 5: The Results
Percent of Elongation
Thermal Expansion
Chart: 
Titanium Ti-6AI-4V | 0.012732 | 0.014551 | 0.016977 | 0.020372 | 0.025465 | 0.033953 | 0.05093 | 0.067906 | 0.10186 | 0.13581 | 0.20372 | 0.40744 | 0.81487 | 1.6297
Copper | 0.010186 | 0.011641 | 0.013581 | 0.016297 | 0.020372 | 0.027162 | 0.040744 | 0.054325 | 0.081487 | 0.10865 | 0.16297 | 0.32595 | 0.6519 | 1.3038
1045 Steel | 0.005093 | 0.0058205 | 0.0067906 | 0.0081487 | 0.010186 | 0.013581 | 0.020372 | 0.027162 | 0.040744 | 0.054325 | 0.081487 | 0.16297 | 0.32595 | 0.6519
2014-T6 Aluminum | 0.015279 | 0.017462 | 0.020372 | 0.024446 | 0.030558 | 0.040744 | 0.061115 | 0.081487 | 0.12223 | 0.16297 | 0.24446 | 0.48892 | 0.97785 | 1.9557
Chart: 
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200 | 220 | 240 | 260 | 280 | 300
2014-T6 Aluminum | 0 | 0.00655 | 0.0131 | 0.01965 | 0.0262 | 0.03275 | 0.0393 | 0.04585 | 0.0524 | 0.05895 | 0.0655 | 0.07205 | 0.0786 | 0.08515 | 0.0917 | 0.09825
1045 Steel | 0 | 0.00361 | 0.00722 | 0.01083 | 0.01444 | 0.01805 | 0.02166 | 0.02527 | 0.02888 | 0.03249 | 0.0361 | 0.03971 | 0.04332 | 0.04693 | 0.05054 | 0.05415
Copper | 0 | 0.00515 | 0.0103 | 0.01545 | 0.0206 | 0.02575 | 0.0309 | 0.03605 | 0.0412 | 0.04635 | 0.0515 | 0.05665 | 0.0618 | 0.06695 | 0.0721 | 0.07725
Titanium Ti-6AI-4V | 0 | 0.002695 | 0.00539 | 0.008085 | 0.01078 | 0.013475 | 0.01617 | 0.018865 | 0.02156 | 0.024255 | 0.02695 | 0.029645 | 0.03234 | 0.035035 | 0.03773 | 0.040425
Notes: In short, here’s my findings. As you can see from the graphs. Aluminum had the highest percent of elongation and thermal expansion.
I calculated the thermal expansion using the coefficient of thermal expansion for each material as specified in the project parameters. I calculated the percent of elongation using the stress from the fatigue analysis and the modulus of elasticity for each material as specified in the project parameters.

## Slide 6: Conclusion
2014-T6 Aluminum: 3/8 inch diameter
1045 Steel: 1/8 inch diameter
Copper: 1/4 inch diameter
Titanium Ti-6AI-4V: 3/8 inch diameter
Notes: Here are the minimum diameters that can be used per material if we want to keep the elongation below 10%. *basically read it off*

## Slide 7: Conclusion
I would choose steel because of it’s superior strength to the others and overall performance.
Steel can be the smallest of the four, but it may be a good idea to make the diameter bigger than necessary if it has the right malleability.
Notes: *basically read off the slide*