## Slide 1: Group 1 Truss project
Presented by Charity Fischer

## Slide 2: Group 1 Truss Project
Participants
  Abdulrahman Almarwan
  Brandon Steup
  Charity Fischer
  Jeanie Hess

## Slide 3: Group 1 Truss Project
Objective
Build a truss
Calculate three force members using the method of sections
Measure the three selected force members using Pasco Universal Interface
Equipment
Pasco truss members
3 load cells
2 1000g weights
Pasco 850 Universal Interface
Jfmatrix.com/analysis

## Slide 4: Group 1 Truss Project
Set-up
Build a truss with
  One end on a roller
  One end on a hinge
  Two points with applied downward force of1000 grams
  That is 72cm wide and 18cm tall
Select three members to solve
  We chose AB, BC, and GD

## Slide 5: Group 1 Truss Project
Procedure
First find the moment about point E to solve for AY
Second find the moment about point G to solve for FBC

## Slide 6: Group 1 Truss Project
Procedure
Solve the sum of forces in the Y direction of a section to find FAB
Solve the sum of forces in the Y direction of a section to find FGD

## Slide 7: Group 1 Truss Project
Procedure
Solve the sum of forces in the Y direction of a section to find FAB
Solve the sum of forces in the Y direction of a section to find FGD

## Slide 8: Group 1 Truss Project
Procedure
Next was the physical experiment using the Pasco Truss members
The 1000g weights were placed in equal distances from the middle and the end of the truss
The load cells attached to the truss were plugged into the Pasco 850 Universal Interface
Five samples of data were taken per load cell
Chart: Forces of AC, BC, and GD Physical Experiment
AB | 1471.4286 | 1462.2449 | 1454.0816 | 1484.6939 | 1475.5102
BC | 1101.0204 | 1109.1837 | 1096.9388 | 1117.3469 | 1113.2653
GD | -46.9388 | -55.102 | -53.0612 | -53.0612 | -47.9592

## Slide 9: Group 1 Truss Project
 | Grams |  | 
 | AB | BC | GD
 | 1471.429 | 1101.02 | -46.9388
 | 1462.245 | 1109.184 | -55.102
 | 1454.082 | 1096.939 | -53.0612
 | 1484.694 | 1117.347 | -53.0612
 | 1475.51 | 1113.265 | -47.9592
Average | 1469.592 | 1107.551 | -51.2245
Results:
AY=1000g
FBC=1000g
FAB=1414g
FGD=0
 | Fab | Fbc | Fgd
Paper | 1414 | 1000 | 0
jfmatrix | 1414.214 | 999.9999 | -0.0002
Physical | 1469.592 | 1107.551 | -51.2245
Average | 1432.602 | 1035.85 | -17.0749
Paper Calculations
Physical Experiment
Jfmatrix Calculations

## Slide 10: Group 1 Truss Project
Observations
  The Force of GD in the real world measurement varied greatly from the results in both our paper calculations and the jfmatrix analysis most likely due to deformation of plastic, angle of load, etc.
  It’s good to work in groups for the sake of checking work and results

## Slide 11: References
http://jfmatrix.com/Analysis
Engineering Mechanics: Statics, r.c. Hibbeler