## Slide 1: EECT 111 Lab Notebook
Nathaniel Paulus & Seth Wills Fall 2017

## Slide 2: Table of Contents
Lab 1 – Resistor Variability
Lab 2 – Reading and Sorting Resistors
Lab 3 – Series Resistors
Lab 4 – Black Box Design
Lab 6 – Black Box Design
Lab 7 – 4 Resistor Parallel Circuit
Lab 8 – Black Box 3 Design
Lab 9 – Series/Parallel Resistors
Lab 10 – Series/Parallel Capacitors
Lab 11 – RC Lab
Lab 12 – Series/Parallel Inductors
Lab 13 – RL Lab

## Slide 3: Lab 1 – Resistor Variability
Date: December 12, 2017
Lab partners: Nathaniel Paulus & Seth Wills
Test equipment: Gwinstek GDM-8245 and HY1802D RSR
Description: In this lab we measured the resistance of 20 1kΩ resistors, and found the average, min, max, standard deviation, etc.
Observations: All the resistors were below the nominal resistance value. It was surprising that none of the resistors were at least 1kΩ.
Lab 1.docx
Lab 1.xlsx

## Slide 4: Lab 1 – Test Measurements
Above are the readings taken for the 20 resistors, along with the calculations.

## Slide 5: Lab 2 – Reading and Sorting Resistors
Date: September 7, 2017
Lab partners: Bianca Shafer & Nathaniel Paulus
Test equipment: Gwinstek GDM-8245
Description: We located 15 resistors of given values, measured their resistance using the multimeter, and recorded their color codes.
Observations: Some of the resistors were not in the right bins.
Lab 2.docx

## Slide 6: Lab 2 – Measured Values and Color Codes

## Slide 7: Lab 3 – Series Resistors
Date: September 14, 2017
Lab partners: Bianca Shafer & Nathaniel Paulus
Test equipment: Gwinstek GDM-8245 and HY1802D RSR
Description: In this lab we measured the total resistance of three series resistors. We also measured the current and the voltage difference at each point in the circuit.
Observations: The measured values were remarkably close to the calculated and simulated values.
Lab 3.docx
Lab 3.xlsx
Lab 3.ms14

## Slide 8: Lab 3 – Schematic

## Slide 9: Lab 3 – Spreadsheet Data

## Slide 10: Lab 3 – Measuring Total Resistance

## Slide 11: Lab 4 – Black Box Design
Date: September 21, 2017
Lab partners: Bianca Shafer & Nathaniel Paulus
Test equipment: Gwinstek GDM-8245 and HY1802D RSR
Description: In this lab we calculated the resistance that would draw 10mA at 9V, and then found three standard resistors that would add to that value when in series.
Observations: None of the available resistors added up to exactly the required resistance. This could be compensated for using a rheostat or potentiometer.
Lab 4.docx
Lab 4.xlsx
Lab 4.ms14

## Slide 12: Lab 4 – Schematic

## Slide 13: Lab 4 – Spreadsheet Calculations
In this spreadsheet we looked for three standard resistor values that would add to 900Ω in series.

## Slide 14: Lab 4 – Completed Circuit
Measuring current.

## Slide 15: Lab 6 – Black Box Design
Date: September 28, 2017
Lab partners: Bianca Shafer & Nathaniel Paulus
Test equipment: Gwinstek GDM-8245 and HY1802D RSR
Description: In this lab we built a parallel circuit with two resistors that would draw 4.6mA at 9V using standard resistor values.
Observations: There are no standard resistors values that would perfectly satisfy the assignment. The closes resistors have a nominal value of 3.9kΩ.
Lab 6.docx
Lab 6.xlsx
Lab 6.ms14

## Slide 16: Lab 6 – Spreadsheet Calculations
Here we calculated the resistance needed for two resistors in parallel to pull 4.6mA.

## Slide 17: Lab 6 – Schematic
Left: Measuring current. Right: Measuring Resistance.

## Slide 18: Lab 7 – 4 Resistor Parallel Circuit
Date: December 12, 2017
Lab partners: Seth Wills & Nathaniel Paulus
Test equipment: Gwinstek GDM-8245 and HY1802D RSR
Description: In this lab we connected four resistors in parallel, and measured and calculated the current that flows through each.
Observations: As resistance increases, current decreases, if voltage stays constant.
Lab 7.docx
Lab 7.xlsx
Lab 7.ms14

## Slide 19: Lab 7 – Spreadsheet Calculations
Here we calculate the current through each branch of the circuit using Ohm’s Law.

## Slide 20: Lab 7 – Schematic

## Slide 21: Lab 7 – Completed Circuit
Green is ground and yellow is 9V.

## Slide 22: Lab 8 – Black Box 3 Design
Date: December 7, 2017
Lab partners: Seth Wills & Nathaniel Paulus
Test equipment: Gwinstek GDM-8245 and HY1802D RSR
Description: In this lab we created a circuit that would produce 1.3V across a black box, using three equal value resistors in parallel in the black box.
Observations: Decreasing the value of R1 leaves more voltage to drop over the other resistors, resulting in an increase in the voltage across R234.
Lab 8.docx
Lab 8.xlsx
Lab 8.ms14

## Slide 23: Lab 8 – Spreadsheet Calculations
Rows 1 through 11 show calculations based on the original schematic. Rows 13 and on show the values that will be taken in order to make 1.3 volts drop over R234.

## Slide 24: Lab 8 – Schematic

## Slide 25: Lab 8 – Completed Circuit, Part 1
The initial resistor configuration, with all 4.7k resistors. The three in the three resistors in parallel are the black box.

## Slide 26: Lab 8 – Completed Circuit, Part 2
Here R1 has been swapped for a potentiometer so that it can equal an exact non-standard resistance, producing 1.3 volts across the black box.

## Slide 27: Lab 9 – Series/Parallel Resistors
Date: October 12, 2017
Lab partners: ­­­­­­­­­­­­­­­­Bianca Shafer & Nathaniel Paulus
Test equipment: Gwinstek GDM-8245 and HY1802D RSR
Description: In this lab we wired up a network of resistors, some in series and some in parallel. We calculated and measured the resistance of each resistor group, and compared them to each other.
Observations: Putting resistors in series increases the total resistance, while putting them in parallel drops their total resistance.
Lab 9.docx
Lab 9.xlsx
Lab 9.ms14

## Slide 28: Lab 9 – Schematic

## Slide 29: Lab 9 – Spreadsheet calculations
Calculating the resistance of each group of resistors.

## Slide 30: Lab 9 – R2 Replaced with Potentiometer

## Slide 31: Lab 10 – Series/Parallel Capacitors
Date: November 16, 2017
Lab partners: Nathaniel Paulus, Seth Wills­­­­­­­­­­­­
Test equipment: Gwinstek GDM-8245, HY1802D RSR, and Gwinstek LCR-819
Description: In this lab we measured three capacitors individually, in series, and in parallel.
Observations: Capacitors in series combine the same way resistors combine in parallel, and capacitors in parallel combine the way resistors combine in series.
Lab 10.docx
Lab 10.xlsx
Lab 10.ms14

## Slide 32: Lab 10 – Spreadsheet Calculations

## Slide 33: Lab 10 – Schematic
Left: Capacitors in parallel. Right: Capacitors series.

## Slide 34: Lab 10 – Completed Circuit, Series

## Slide 35: Lab 10 – Completed Circuit, Parallel

## Slide 36: Lab 11 – RC Lab
Date: November 16, 2017
Lab partners: Nathaniel Paulus, Seth Wills­­­­­­­­­­­­
Test equipment: Gwinstek GDM-8245, Gwinstek LCR-819, Tektronix DS 220, Gwinstek GFG-8210
Description: In this lab we measured the output voltage of three different capacitors given various frequencies.
Observations: Voltage is lowest when frequency is highest.
Lab 11.docx
Lab 11.xlsx
Lab 11.ms14

## Slide 37: Lab 11 - Schematic

## Slide 38: Lab 11 – Multisim Graph

## Slide 39: Lab 11 – Graph of Lab Measurements
Chart: 0.47uF Frequency v Voltage (mV)
| 10 | 100 | 300 | 500 | 700 | 900 | 2000 | 4000 | 6000 | 8000 | 10000
 | 1020 | 960 | 740 | 560 | 440 | 360 | 184 | 104 | 72 | 58 | 48
Chart: 1.0uF Frequency v Voltage (mV)
| 50 | 200 | 400 | 600 | 800 | 1000 | 3000 | 5000 | 7000 | 9000 | 10000
 | 980 | 672 | 424 | 296 | 228 | 188 | 74 | 45.6 | 34.4 | 26.8 | 24.8
Chart: 2.2uF Frequency v Voltage (mV)
| 50 | 200 | 400 | 600 | 800 | 1000 | 3000 | 5000 | 7000 | 9000 | 10000
 | 800 | 304 | 164 | 114 | 88 | 74 | 29 | 19.6 | 15.6 | 11.4 | 11
These graphs show the relation between the frequency and output voltage of RC circuits using various values of capacitors. Frequency in the graphs maxes at 10kHz. The 0.47uF graph starts at 10Hz, while the other two start at 50Hz. The y axis shows output voltage divided by input voltage, in mV.

## Slide 40: Lab 11 – Measuring with Oscilloscope

## Slide 41: Lab 11 – Oscilloscope Measurement

## Slide 42: Lab 12 – Series/Parallel Inductors
Date: December 7, 2017
Lab partners: Nathaniel Paulus, Seth Wills­­­­­­­­­­­­
Test equipment: Gwinstek LCR-819
Description: In this lab we measured the inductance of three inductors, individually, in series, and in parallel.
Observations: Inductance increases when put in series, and decreases when put in parallel, in the same way resistors combine.
Lab 12.docx
Lab 12.xlsx
Lab 12.ms14

## Slide 43: Lab 12 – Spreadsheet Calculations
Inductors in series and parallel.

## Slide 44: Lab 12 – Schematic
Left: Inductors measured in series. Right: Inductors measured parallel.

## Slide 45: Lab 12 – Measuring Inductance

## Slide 46: Lab 12 – Measuring Inductors in Series
Measuring inductance in series.

## Slide 47: Lab 12 – Measuring Inductors in Parallel
Measuring inductance in parallel.

## Slide 48: Lab 13 – RL Lab
Date: December 7, 2017
Lab partners: ­­­­­­­­­­­­­­­­Nathaniel Paulus, Seth Wills
Test equipment: Gwinstek GDM-8245, Tektronix TDS 220, Gwinstek GFG-8210, and Gwinstek LCR-819
Description: In this lab we measured the output voltage of three inductors across a wide range of frequencies.
Observations: The values we recorded in the lab (up to 10kHz) were sufficient to show the first half of the graph produced by Multisim, but the data was just beginning to flatten out at 10kHz (or not even started to flatten), so the second part was nearly invisible.
Lab 13.docx
Lab 13.xlsx
Lab 13.ms14

## Slide 49: Lab 13 – Schematic

## Slide 50: Lab 13 – Multisim Graph

## Slide 51: Lab 13 – Graph of Lab Measurements
These graphs show the relation between the frequency and output voltage of RL circuits using various values of inductors. Frequency in the graphs ranges from 50Hz to 10kHz. The y axis shows output voltage divided by input voltage, in mV.
Chart: 1.0mH Frequency v. Voltage (mV)
| 50 | 200 | 400 | 600 | 800 | 1000 | 3000 | 5000 | 7000 | 9000 | 10000
 | 23 | 26 | 34 | 44 | 56 | 68 | 182 | 296 | 416 | 512 | 544
Chart: 2.2mH Frequency v. Voltage (mV)
| 50 | 200 | 400 | 600 | 800 | 1000 | 3000 | 5000 | 7000 | 9000 | 10000
 | 40.8 | 52 | 68 | 84 | 112 | 132 | 348 | 456 | 576 | 688 | 728
Chart: 4.7mH Frequency v. Voltage (mV)
| 50 | 200 | 400 | 600 | 800 | 1000 | 3000 | 5000 | 7000 | 9000 | 10000
 | 76 | 88 | 120 | 162 | 204 | 256 | 648 | 728 | 848 | 900 | 940