## Slide 1: Lab 6
Capacitors

## Slide 2: Slide master
Purpose – To measure the values of capacitors in series and parallel circuits
Materials – Breadboard, 1uf, .47uf, and .1uf capacitors, Misc. wires
Tools – 2 LCR meters (BK857b, LCR-819)
Procedure – build the circuit on the breadboard. Measure and record C1,C2,C3, and Ct.

## Slide 3: Circuit

## Slide 4: Sim Results
Parallel |  | 
C1 = | 1.0E-6 | 
C2 = | 470.0E-9 | 
C3 = | 100.0E-9 | 
Ct = | 1.57E-06 | B23+B24+B25
Series |  | 
C1 = | 1.0E-6 | 
C2 = | 470.0E-9 | 
C3 = | 100.0E-9 | 
Ct = | 76.2E-9 | 1/((1/B3)+(1/B2)+(1/B4))

## Slide 5: Results
 |  | Measured values | 
 | calculated | BK-857b | LCR-819
 | 1uf | 1.112uf | 1007nf
 | .47uf | 512nf | 413nf
 | .1uf | .108uf | 98nf
Ct parallel | 1.57uf | 1.621uf | 1516.2nf
Ct series | 76.17504nf | 84nf | 73.4nf

## Slide 6: Lab Book Scan