## Slide 1: Lab 7
Basic stamp binary led counter
By: Matthew Krueger

## Slide 2: Lab 7
Directive
Build a circuit that uses 4 LEDs to count from 0 to 15 in binary, using the LEDs as digits, (off = 0, on = 1).
Ex. #1 in Binary is 0001, light LEDs off-off-off-on

## Slide 3: Lab 7
Parts List
    Basic Stamp
    4x LED
    4x 470Ω Resistors
    Misc wires

## Slide 4: Lab 7
Schematic

## Slide 5: Lab 7
Circuit

## Slide 6: Lab 7
Program
'{$STAMP BS2}
'{$PBASIC 2.0}
'Program 1
LED1 CON 0
LED2 CON 1
LED3 CON 3
LED4 CON 4
OUTPUT 0
OUTPUT 1
OUTPUT 2
OUTPUT 3
LOW LED1
LOW LED2
LOW LED3
LOW LED4
HIGH LED4
HIGH LED3
HIGH LED2
HIGH LED1
PAUSE 1000
LOW LED4
LOW LED3
LOW LED2
LOW LED1
PAUSE 2000
HIGH LED4
PAUSE 1000
LOW LED4
HIGH LED3
PAUSE 1000
LOW LED3
HIGH LED4
HIGH led3
PAUSE 1000
LOW LED4
LOW led3
HIGH led2
PAUSE 1000
LOW led2
HIGH LED2
HIGH LED4
PAUSE 1000
LOW LED2
LOW LED4
HIGH LED2
HIGH LED3
PAUSE 1000
LOW LED2
LOW LED3
HIGH LED2
HIGH LED3
HIGH LED4
PAUSE 1000
LOW LED2
LOW LED3
LOW LED4
HIGH LED1
PAUSE 1000
LOW LED1
HIGH LED1
HIGH LED4
PAUSE 1000
LOW LED1
LOW LED4
HIGH LED1
HIGH LED3
PAUSE 1000
LOW LED1
LOW LED3
HIGH LED1
HIGH LED3
HIGH LED4
PAUSE 1000
LOW LED1
LOW LED3
LOW LED4
HIGH LED1
HIGH LED2
PAUSE 1000
LOW LED1
LOW LED2
HIGH LED1
HIGH LED2
HIGH LED4
PAUSE 1000
LOW LED1
LOW LED2
LOW LED4
HIGH LED1
HIGH LED2
HIGH LED3
PAUSE 1000
LOW LED1
LOW LED2
LOW LED3
HIGH LED1
HIGH LED2
HIGH LED3
HIGH LED4
PAUSE 1000
LOW LED1
LOW LED2
LOW LED3
LOW LED4

## Slide 7: Lab 7
Results - video

## Slide 8: Lab 7
Results: Experiment was successful, LEDs light in sequence counting in binary from 0 to 15.

## Slide 9: Lab 7
After doing some research, a simpler code was found.
' {$STAMP BS2}
' {$PBASIC 2.5}
LEDs VAR OUTL ' on P0 - P7
counter VAR Byte
Reset:
DIRL = %11111011 ' make P0 - P7 outputs·
Main:
FOR counter = 0 TO 15
LEDs = counter
PAUSE 1000
NEXT
GOTO Main