## Slide 1: EECT 111 – Lab Notebook
Zach Anderson
Circuit Analysis
May 7, 2015

## Slide 3: Table of Contents
Lab 1 - Resistor Variability
Lab 2 – Reading and Sorting Resistors
Lab 3 – Series Resistors
Lab 4 – Black Box Design
Lab 5 - Black Box Design 2
Lab 6- non existent
Lab 7 – 4 Parallel Resistor Circuit
Lab 8 – Black Box Design 3
Lab 9 – Series/Parallel Resistors
Lab 10 - Series/Parallel Capacitors
Lab 11 – RC Lab
Lab 12 - Series/Parallel Inductors
Lab 1 –
Lab 2 – 1/29/15
Lab 3 – 1/29/15
Lab 4 – 2/12/15
Lab 5 - 2/19/15
Lab 6- non existent
Lab 7 – 2/26/15
Lab 8 – 2/26/15
Lab 9 –3/19/15
Lab 10 – 4/2/15
Lab 11 – 4/9/15
Lab 12 – 4/23/15
Lab 1 – 4
Lab 2 –11
Lab 3 –17
Lab 4 –24
Lab 5 - 31
Lab 6- non existent
Lab 7 – 40
Lab 8 –48
Lab 9 –54
Lab 10 – 64
Lab 11 –71
Lab 12 –80
LAB
Date
SLIDE NUMBER

## Slide 4: Lab 1 – Resistor Variability

## Slide 5: Lab 1 – Resistor Variability
Purpose
The purpose of this lab was to learn how resistors vary using 20 resistors with the same color code
Equipment
Digital Multimeter
  Make-GW instek
  Model-GDM-8245
  SN-CL860237
20 – 1 kΩ resistors

## Slide 6: Lab 1 – Resistor Variability
Procedure
In two person groups, we took ten 1k Ohm resistors and measured their actual resistance using an Ohmmeter.
This information was recorded on our provided handouts.
We then took the information gathered back to the classroom where we created an Excel sheet documenting and charting our findings.
.

## Slide 7: Lab 1 – Resistor Variability 1/15/15
Resistor Variability |  |  | Tolerance |  | 
Sample | Measured Value (kOhm) | Ohm | High | Low | Nominal
1 | 0.979 | 979 | 1050 | 950 | 1000
2 | 0.982 | 982 | 1050 | 950 | 1000
3 | 0.978 | 978 | 1050 | 950 | 1000
4 | 0.979 | 979 | 1050 | 950 | 1000
5 | 0.999 | 999 | 1050 | 950 | 1000
6 | 0.987 | 987 | 1050 | 950 | 1000
7 | 0.987 | 987 | 1050 | 950 | 1000
8 | 0.982 | 982 | 1050 | 950 | 1000
9 | 0.98 | 980 | 1050 | 950 | 1000
10 | 1 | 1000 | 1050 | 950 | 1000
11 | 0.977 | 977 | 1050 | 950 | 1000
12 | 0.985 | 985 | 1050 | 950 | 1000
13 | 0.996 | 996 | 1050 | 950 | 1000
14 | 0.977 | 977 | 1050 | 950 | 1000
15 | 0.983 | 983 | 1050 | 950 | 1000
16 | 0.981 | 981 | 1050 | 950 | 1000
17 | 0.994 | 994 | 1050 | 950 | 1000
18 | 0.979 | 979 | 1050 | 950 | 1000
19 | 0.975 | 975 | 1050 | 950 | 1000
20 | 0.978 | 978 | 1050 | 950 | 1000
21 | 0.98 | 980 | 1050 | 950 | 1000
22 | 0.979 | 979 | 1050 | 950 | 1000
23 | 0.978 | 978 | 1050 | 950 | 1000
24 | 0.977 | 977 | 1050 | 950 | 1000
25 | 0.978 | 978 | 1050 | 950 | 1000
26 | 0.979 | 979 | 1050 | 950 | 1000
27 | 0.977 | 977 | 1050 | 950 | 1000
28 | 0.979 | 979 | 1050 | 950 | 1000
29 | 0.981 | 981 | 1050 | 950 | 1000
30 | 0.983 | 983 | 1050 | 950 | 1000
31 | 0.982 | 982 | 1050 | 950 | 1000
32 | 0.98 | 980 | 1050 | 950 | 1000
33 | 0.981 | 981 | 1050 | 950 | 1000
34 | 0.984 | 984 | 1050 | 950 | 1000
35 | 0.978 | 978 | 1050 | 950 | 1000
36 | 0.98 | 980 | 1050 | 950 | 1000
37 | 0.98 | 980 | 1050 | 950 | 1000
38 | 0.98 | 980 | 1050 | 950 | 1000
39 | 0.981 | 981 | 1050 | 950 | 1000
40 | 0.982 | 982 | 1050 | 950 | 1000
41 | 0.982 | 982 | 1050 | 950 | 1000
42 | 0.98 | 980 | 1050 | 950 | 1000
43 | 0.978 | 978 | 1050 | 950 | 1000
44 | 1.002 | 1002 | 1050 | 950 | 1000
45 | 0.99 | 990 | 1050 | 950 | 1000
46 | 0.978 | 978 | 1050 | 950 | 1000
47 | 0.979 | 979 | 1050 | 950 | 1000
48 | 1.001 | 1001 | 1050 | 950 | 1000
49 | 0.98 | 980 | 1050 | 950 | 1000
50 | 0.99 | 990 | 1050 | 950 | 1000
51 | 0.984 | 984 | 1050 | 950 | 1000
52 | 0.983 | 983 | 1050 | 950 | 1000
53 | 0.984 | 984 | 1050 | 950 | 1000
54 | 0.982 | 982 | 1050 | 950 | 1000
55 | 0.978 | 978 | 1050 | 950 | 1000
56 | 0.983 | 983 | 1050 | 950 | 1000
57 | 0.984 | 984 | 1050 | 950 | 1000
58 | 0.981 | 981 | 1050 | 950 | 1000
59 | 0.981 | 981 | 1050 | 950 | 1000
60 | 0.978 | 978 | 1050 | 950 | 1000
61 | 0.98 | 980 | 1050 | 950 | 1000
62 | 0.984 | 984 | 1050 | 950 | 1000
63 | 0.981 | 981 | 1050 | 950 | 1000
64 | 0.982 | 982 | 1050 | 950 | 1000
65 | 0.984 | 984 | 1050 | 950 | 1000
66 | 0.982 | 982 | 1050 | 950 | 1000
67 | 0.984 | 984 | 1050 | 950 | 1000
68 | 0.98 | 980 | 1050 | 950 | 1000
69 | 0.987 | 987 | 1050 | 950 | 1000
70 | 0.981 | 981 | 1050 | 950 | 1000

## Slide 8: Lab 1 – Resistor Variability
Equipment Needed |  |  |  | 
Digital Multimeter |  |  |  | 
Make: | GW Instek |  |  | 
Model: | GDM - 8245 |  |  | 
SN: | CL860237 |  |  | 
Resistor Color Code = | Brown, Black, Red, Gold |  |  | 
Resistor value = | 1000 | Ohm | 1 | k Ohm
Resistor Tolerance = |  |  | 5 | %
Using Excel, plot the resistor values and find: |  |  |  | 
Smallest resistance = | 975 | Ohm | 0.975 | k Ohm
Largest resistance = | 1002 | Ohm | 1.002 | k Ohm
Average resistance = | 982.6 | Ohm | 0.9826 | k Ohm
Standard Deviation = | 5.822 | Ohm | 0.00582 | k Ohm
Median = | 981 | Ohm | 0.981 | k Ohm
Mode = | 980 | Ohm | 0.98 | k Ohm
Range = | 27 | Ohm | 0.027 | k Ohm
Do any resistor values exceed the part tolerance? |  |  |  | No

## Slide 9
Chart: Resistor Variability
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Measured Values | 979 | 982 | 978 | 979 | 999 | 987 | 987 | 982 | 980 | 1000
High Tolerance | 1050 | 1050 | 1050 | 1050 | 1050 | 1050 | 1050 | 1050 | 1050 | 1050
Low Tolerance | 950 | 950 | 950 | 950 | 950 | 950 | 950 | 950 | 950 | 950
Nominal Value | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000
Chart: Resistor Variability

## Slide 10: Lab 1 - Conclusion
Summary
We initially measured the values of 5 different 1000 ohm resistors. After passing out the resistors, there were enough for 10 resistors a group. After each group measured their 10 resistors, each group sent their data to each other. A new total of 70 resistor values was plotted. All 70 of the resistor samples were within the part tolerance (50 Ohms). The majority of the samples fell under the nominal value of 1000 ohms. There are only three resistors that equaled 100 or over. The median value came out to be 981 ohms and the mode was 980 ohms. The difference between the high and the low, or the range, was 27 ohms.

## Slide 11: Lab 2 – Reading and Sorting Resistors

## Slide 12: Lab 2 – Reading and Sorting Resistors
Purpose
The purpose of this lab was to learn the resistor color code using 15 resistors which must be sorted from smallest to largest value. Build a resistor kit that includes 15 resisters and sort resistors based on color code from smallest to largest and measure the resistance of each resistor and verify sorting.
Equipment
Digital Multimeter
  Make-GW instek
  Model-GDM-8245
  SN-CL860237
15 –resistors

## Slide 13: Lab 2 – Reading and Sorting Resistors
Procedure
We broke up into two person groups and found the 15 resistors described on the provided hand out.
We then used the resistor color code to sort the resistors from smallest to largest.
After sorting the resistors, we used a digital multimeter to verify our sorting.
After measuring the resistors, we also made an Excel sheet showing that all resistors were within tolerance.

## Slide 14: Lab 2 – Resistor Color Codes
Zach Anderson Lab 2, 1/29/15, Reading and Sorting Resistors |  |  |  |  |  |  |  |  |  |  |  | 
 | Value | Measured | Tolerance | Min | Max | Within Tolerance | Too High, man | Too Low | Color Code |  |  | 
1 | 100 | 98.2 | 0.05 | 95 | 105 | Yes | No | No | BROWN | BLACK | BROWN | GOLD
2 | 220 | 216.2 | 0.05 | 209 | 231 | Yes | No | No | RED | RED | BROWN | GOLD
3 | 330 | 322 | 0.05 | 313.5 | 346.5 | Yes | No | No | ORANGE | ORANGE | BROWN | GOLD
4 | 470 | 462.6 | 0.05 | 446.5 | 493.5 | Yes | No | No | YELLOW | VIOLET | BROWN | GOLD
5 | 1000 | 983.5 | 0.05 | 950 | 1050 | Yes | No | No | BROWN | BLACK | RED | GOLD
6 | 2200 | 2193 | 0.05 | 2090 | 2310 | Yes | No | No | RED | RED | RED | GOLD
7 | 3300 | 3218 | 0.05 | 3135 | 3465 | Yes | No | No | ORANGE | ORANGE | RED | GOLD
8 | 4700 | 4598 | 0.05 | 4465 | 4935 | Yes | No | No | YELLOW | VIOLET | RED | GOLD
9 | 10000 | 9820 | 0.05 | 9500 | 10500 | Yes | No | No | BROWN | BLACK | ORANGE | GOLD
10 | 22000 | 21560 | 0.05 | 20900 | 23100 | Yes | No | No | RED | RED | ORANGE | GOLD
11 | 33000 | 32900 | 0.05 | 31350 | 34650 | Yes | No | No | ORANGE | ORANGE | ORANGE | GOLD
12 | 47000 | 45660 | 0.05 | 44650 | 49350 | Yes | No | No | YELLOW | VIOLET | ORANGE | GOLD
13 | 100000 | 100150 | 0.05 | 95000 | 105000 | Yes | No | No | BROWN | BLACK | YELLOW | GOLD
14 | 1000000 | 1028000 | 0.05 | 950000 | 1050000 | Yes | No | No | BROWN | BLACK | GREEN | GOLD
15 | 10000000 | 10040000 | 0.05 | 9500000 | 10500000 | Yes | No | No | BROWN | BLACK | BLUE | GOLD
Example | Value | Measured | Tolerance | Min | Max | Within Tolerance | Too High, man | Too Low |  |  |  | 
16 | 10 | 8 | 0.05 | 9.5 | 10.5 | No | No | Yes |  |  |  | 
17 | 20 | 25 | 0.05 | 19 | 21 | No | Yes | No |  |  |  | 

## Slide 15
Chart: Resistors 1-8
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Measured | 98.2 | 216.2 | 322 | 462.6 | 983.5 | 2193 | 3218 | 4598
Min | 95 | 209 | 313.5 | 446.5 | 950 | 2090 | 3135 | 4465
Max | 105 | 231 | 346.5 | 493.5 | 1050 | 2310 | 3465 | 4935
Chart: Resistors 9-13
| 9 | 10 | 11 | 12 | 13 | 14 | 15
Measured | 9820 | 21560 | 32900 | 45660 | 100150 | 1028000 | 10040000
Max | 10500 | 23100 | 34650 | 49350 | 105000 | 1050000 | 10500000
Min | 9500 | 20900 | 31350 | 44650 | 95000 | 950000 | 9500000

## Slide 16: Lab 2 - Conclusion
Summary:
We found that we had correctly sorted all of our resistors.
We also found that all of the sorted resistors had the same tolerance (5%)

## Slide 17: Lab 3 – Series Resistors Current and Voltage

## Slide 18: Lab 3- Series Resistors Current and Voltage
Purpose
The purpose of this lab was to experiment with the series circuits and verify that the simulation, analysis, and measured test results all agree.
Equipment
Digital Multimeter
  Make-GW instek
  Model-GDM-8245
  SN-CL860237
3 –resistors
  10 kΩ, 2.2kΩ, 4.7kΩ
Elviss II
  Make-NI
  Model-GDM-8245
  SN-CL860264

## Slide 19: Lab 3 – Series Resistors Current and Voltage
Procedure
We will be building a simple series circuit using the Elvis II board and three resistors, a 10KΩ, a 2.2KΩ, and a 4.7KΩ.
We will calculate the total resistance of this circuit in Excel, Multisim, and on the Elvis II board in the lab.

## Slide 20: Lab 3 – Series Resistors Current and Voltage
 | Measured | Calculated | Simulated | 
R1 | 97.8E+3 | 10.0E+3 | 10.0E+3 | Ω
R2 | 2.22E+3 | 2.20E+3 | 2.20E+3 | Ω
R3 | 4.61E+3 | 4.70E+3 | 4.70E+3 | Ω
RT | 16.6E+3 | 16.9E+3 | 16.9E+3 | Ω
IT | 542.2E-6 | 532.5E-6 | 532.9E-6 | Amps
V1 | 9.00E+0 | 9.00E+0 | 9.00E+0 | volts
VA | 5.32E+0 | 5.33E+0 | 5.33E+0 | volts
VB | 1.17E+0 | 1.17E+0 | 1.17E+0 | volts
VC | 2.51E+0 | 2.51E+0 | 2.50E+0 | volts

## Slide 21: Lab 3 – Multisim Examples

## Slide 22: Lab 3 – Multisim Examples

## Slide 23: Lab 3 - Conclusion
Summary:
Our results from Excel, Multisim, and in-lab measurements all agreed.

## Slide 24: Lab 4 – Black Box Design

## Slide 25: Lab 4- Black Box Design
Purpose
The purpose of this lab was to learn about series circuits.
Equipment
Digital Multimeter
  Make-GW instek
  Model-GDM-8245
  SN-CL860334
3 –resistors
  Standard
Elvis II
  Make-Nation Instruments
  Model-NI ELVIS II
  SN-166CF1

## Slide 26: Lab 4 – Black Box Design
Procedure
We were given a hand out that contained a picture of a circuit with part of the circuit blacked out. We will use the information that is not blacked out, to figure out what components are blacked out.
We will be doing calculations of this circuit in Excel and Multisim. We will then build the circuit in the lab.

## Slide 27: Lab 4 – Black Box Design

## Slide 28: Lab 4 – Black Box Design
Equations Used
Series Resistors
V = IR
Ohm’s Law

## Slide 29: Lab 4 - Multisim

## Slide 31: Lab 4 - Conclusion
Summary:
By using what we already knew about the circuit, we were able to figure out what parts of the circuit were covered by the “black box”.

## Slide 32: Lab 5 – Black Box Design

## Slide 33: Lab 5- Black Box Design
Purpose
The purpose of this lab was to learn about parallel circuits
Equipment
Digital Multimeter
  See slide 24
3 –resistors
  Standard
Elviss II
  See slide 24

## Slide 34: Lab 5 – Black Box Design
Procedure
We will use the information given about the circuit to figure out what components are being hidden under the black box.
We will use Excel & Multisim to calculate and simulate what components may be missing. We will then build the circuit in the lab to verify that we are correct.

## Slide 35: Lab 5 – Black Box Design in Parallel
V1= | 9 | V |  |  |  | 
It= | 4.64E-03 | A |  |  |  | 
Rt=V/It |  | Ω |  |  |  | 
Rt= | 1938.819474 | Ω |  |  |  | 
Choose R1 |  |  |  |  |  | 
R2=Rt/(1-(Rt/R1)) |  | Ω |  |  |  | 
R1= | 4000 | Ω |  |  |  | 
R2= | 3762.541806 | Ω |  |  |  | 
 | Design | Measured | Calculated | Simulated | 3 resistors | 
V1= | 9 | 9.005 | 9 | 9 | 9.004 | V
It= | 4.642 | 4.4288 | 4.642 | 4.642 | 4.6308 | mA
Rt= | 1938.82 | 1932.2 | 1938.819474 | 1939 | 1842.2 | Ω
R1= | 4000 | 3862.4 | 4000 | 4000 | 5592.7 | Ω
R2= | 3762.5438 | 3862.1 | 3762.541806 | 3762.543786 | 6782.1 | Ω
 |  |  |  |  | 4618.9 | Ω

## Slide 36: Lab 5 – Black Box Design in Parallel
Equipment Needed |  |  |  | 
Digital Multimeter |  |  |  | 
Make: | GW Instek |  |  | 
Model: | GDM - 8245 |  |  | 
SN: | CL860237 |  |  | 
Resistor Color Code = | Orange, White, Red, Gold |  |  | 
Resistor value = | 3900 | Ohm |  | 
Resistor Tolerance = | 5 | % |  | 
5% of design Rt= | 96.941 | Ω |  | 
Rt - 5%= | 1841.879 |  |  | 
3 resistors Rt= | 1842.2 |  |  | 
Percent off= | 0.049834435 |  |  | 
 | 4.983443538 | % |  | 

## Slide 37: Lab 5 – Black Box Design
V = IR
Equations Used
Two Resistors In Parallel
Ohm’s Law

## Slide 38: Lab 5 - Multisim

## Slide 39: Lab 5 - Visual

## Slide 40: Lab 5 - Conclusion
Summary:
Using the information provided about the circuit, we were able to determine what components were hidden under the black box.

## Slide 41: Lab 6 – Nothing

## Slide 42: Lab 7 – Parallel Resistor Circuit

## Slide 43: Lab 7- 4 Parallel Resistor Circuit
Purpose
The purpose of this lab was to learn about parallel circuits
Equipment
Digital Multimeter
  Make-GW instek
  Model-GDM-8245
  SN-CL860334
3 –resistors
  Standard
Elviss II
  Make-Nation Instruments
  Model-NI ELVIS II
  SN-166CF1

## Slide 44: Lab 7 – Parallel Resistor Circuit
Procedure
We will calculate the values of a circuit containing resistors in parallel.
We will calculate the values in Excel, simulate the circuit in Multisim, and measure the actual circuit in the lab.

## Slide 45: Lab 7 – 4 Parallel Resistor Circuit

## Slide 46: Lab Seven – Parallel Resistor Circuit
Equations Used
V = IR
Parallel
Ohm’s Law

## Slide 47: Lab 7 - Multisim

## Slide 48: Lab 7 - Multisim

## Slide 49: Lab 7 -Visual

## Slide 50: Lab 7 - Conclusion
Summary:
We found our calculations in Excel, simulation in Multisim, and measurements done in the lab to all agree.

## Slide 51: Lab 8 – Black Box Design 3

## Slide 52: Lab 8- Black Box 3
Purpose
The purpose of this lab was to learn about building a circuit that produces exactly 1.3V. We will need to use what we already know about the circuit to determine what components are hidden under the black box.
Equipment
Digital Multimeter
  Make-GW instek
  Model-GDM-8245
  SN-CL860334
3 –resistors, 1 – 10kohm potentiometer
  Standard
Elviss II
  Make-Nation Instruments
  Model-NI ELVIS II
  SN-166CF1

## Slide 53: Lab 8 – Black Box 3

## Slide 54: Lab Eight – Black Box Design
Equations Used
V = IR
Parallel
Series
Ohm’s Law

## Slide 55: Lab 8 - Visual

## Slide 56: Lab 8 - Multisim

## Slide 57: Lab 8 - Conclusion
Summary:
We initially used the wrong resistance in this lab. Through a misunderstanding with our professor, we used the wrong data and needed to re-do this lab
After using the correct information and parts, we found our calculations in Excel, simulation in Multisim, and measurements done in the lab to all agree.

## Slide 58: Lab 9 – Series/Parallel Resistors

## Slide 59: Lab 9 – Series/Parallel Resistors
Purpose
The purpose of this lab was to experiment with the series circuits and verify that the simulation, analysis, and measured test results all agree.
Equipment
Digital Multimeter
  Make-GW instek
  Model-GDM-8245
  SN-CL860237
8 –resistors
  2 x 10 kΩ, 2 x 2.2kΩ, 4.7kΩ
Elviss II
  Make-GW instek
  Model-GDM-8245
  SN-CL860237

## Slide 60: Lab 9 – Series/Parallel Resistors
Procedure
We will be analyzing the circuit provided in the Lab 9 hand out. We will be calculating the resistance of the circuit in Excel and simulating the resistance of the circuit in Multisim. We will then build the circuit in the lab and take measurements.

## Slide 61: Lab 9 – Series/Parallel Resistors
Equations Used
Series
Parallel

## Slide 62: Lab 9 – Series/Parallel Resistors

## Slide 63: Lab 9 – Series/Parallel Resistors

## Slide 64: Lab 9 - Multisim

## Slide 65: Lab 9 - Multisim

## Slide 66: Lab 9 - Multisim

## Slide 67: Lab 9 –Series Parallel Resistors

## Slide 68: Lab 9 - Conclusion
Summary:
We found our calculations in Excel, simulation in Multisim, and measurements done in the lab to all agree.

## Slide 69: Lab 10 – Series/ Parallel Capacitors

## Slide 70: Lab 10 – Series/Parallel Capacitors
Purpose
The purpose of this lab was to experiment with series and parallel combinations of capacitors.
Equipment
LCR meter
  Make- GW instek
  Model-LCR meter 819
  SN-E120997
8 –resistors
  2 x 10 kΩ, 2 x 2.2kΩ, 4.7kΩ
Elviss II
  Make-GW instek
  Model-GDM-8245
  SN-CL860237

## Slide 71: Lab 10 – Series/ Parallel Capacitors
Procedure:
We will be measuring the capacitance of capacitors using an LCR meter. We will then combine capacitors in series and in parallel. We will use Excel and Multisim to calculate and simulate what the capacitance of a series circuit and a parallel circuit should be, we will then build the circuits in the lab and measure.

## Slide 72: Lab 10 – Series/Parallel Capacitors
Equations Used
Parallel
Series

## Slide 73: Lab 10 – Series/Parallel Capacitors

## Slide 74: Lab 10 – Series/Parallel Capacitors

## Slide 75: Lab 10 - Visual
Parallel
Series

## Slide 76: Lab 10 – Conclusion
Summary:
When we went to the lab to build and measure our circuits, we found that our results matched what we were expecting.
This showed us that our simulations and calculations were done correctly.

## Slide 77: Lab 11 – RC Lab

## Slide 78: Lab 11 – RC Lab
Purpose
The purpose of this lab was to experiment with RC circuits.
Equipment
Oscilloscope
Function Generator
LCR meter
  Make- GW instek
  Model-LCR meter 819
  SN-E120997
Resistor – 1 kΩ
  SN-CL860237
Digital Multimeter
  Make-GW instek
  Model-GDM-8245
  SN-CL860237
LCR meter
  Make-
  Model-
  SN-
3 capacitors
  0.47 uF, 1 uF, 2.2 uF
Elviss II
  Make-GW instek
  Model-GDM-8245
  SN-CL860237

## Slide 79: Lab 11 – RC Lab
Procedure:
The information we used to carry out this lab was obtained from the book and in class lectures.

## Slide 80: Lab 11 – RC Lab
Equations Used

## Slide 83: Lab 11 - Multisim

## Slide 84: Lab 11 - Multisim

## Slide 85: Lab 11 - Visual

## Slide 86: Lab 11 - Conclusion
Summary:
We found our calculations in Excel, simulation in Multisim, and measurements done in the lab to all agree.

## Slide 87: Lab 12 – Series/ Parallel Inductors

## Slide 88: Lab 12 – Series/Parallel Inductors
Purpose
The purpose of this lab was to experiment with series and parallel combinations of inductors.
Equipment
LCR meter
  Make- GW instek
  Model-LCR meter 819
  SN-E120997
3 –inductors
  1 mH, 2.2 mH, 4.7 mH
Elviss II
  Make-GW instek
  Model-GDM-8245
  SN-CL860237

## Slide 89: Lab 12 – Series/ Parallel Inductors
Procedure
The information needed to conduct this experiment was gathered from the instructor and the book.
We will set up and measure three inductors in a series circuit and in a parallel circuit.
We will calculate what the inductance of both circuits should be in Excel, simulate the circuits in Multisim, and take actual measurements in the lab.

## Slide 90: Lab 12 – Series/Parallel Inductors
Equations Used
Series
Parallel

## Slide 91: Lab 12 – Series/Parallel Inductors

## Slide 92: Lab 12 – Series/Parallel Inductors

## Slide 93: Lab 12 - Multisim

## Slide 94: Lab 12 - Measurements

## Slide 95: Lab 12 - Visual
Series
Parallel

## Slide 96: Lab 12 - Conclusion
Summary:
We calculated and simulated both circuits, then built and measured the circuits in the lab.
Our calculations and simulations were correct.

## Slide 97: In conclusion
All in all, taking EECT 111, I was able to expand my knowledge of the intricacies of circuits. I have not only gained a better understanding of approaching, handling, and the math of circuits, but gained a lifelong appreciation for something that will be very useful in the real world. Thank you