## Slide 1: Lab 0
By: Chad Creager
Lab Partner:
Instructor: A Bell
Class: EECT 122
Date: 8/31/15

## Slide 2: Objectives:
To test one gate on 74LS08 AND GATE.

## Slide 3: Equipment and Parts:
Bench 3
HY1802D Power Supply
GWINSTEK Multi Meter Ser # CL860260
Bread Board
Dip Switches
2- 1KOHM Resistors
1- 74LS08N
1 Green LED
Wires

## Slide 4: Theories:
X * 1 = X which is Theorem 1
X * 0 = 0 which is Theorem 2
Y * 1 = Y which is Theorem 1
Y * 0 = 0 which is Theorem 2

## Slide 5: Data/Lab Results/Simulations/Schematics:
When both switches are open output is low.
When one or the other switch is closed output is low.
When both switches are closed output is high.

## Slide 9: Multisim

## Slide 10: Troubleshooting:
Used Multimeter to test all input levels and output levels.
Tested output with a load and without.

## Slide 11: Conclusion:
The 74LS08N Gate worked as expected.
The output voltage was higher without a load than it was with a load when the output was high. When the output was low the measured voltage was the same loaded or unloaded.
With output high the voltage was 4.05 V unloaded and 2.22 V loaded
Tested with Vcc at 4.75V and checked High output not loaded and got 3.55V this matches the results on the data sheet.

## Slide 12: Data Sheets:

## Slide 15: Lab 1
By: Chad Creager
Lab Partner:
Instructor: A Bell
Class: EECT 122
Date: 9/14/15

## Slide 16: Objectives:
Design build and test a 3 input “AND” and “OR”

## Slide 17: Equipment and Parts:
Bench 3
HY1802D Power Supply
GWINSTEK Multi Meter Ser # CL860260
Bread Board
Dip Switches
3- 1KOHM Resistors
1- 74LS08N and 174LS32
1 Green LED
Wires

## Slide 18: Theories:

## Slide 19: Data/Lab Results/Simulations/Schematics:
The And gates had to have all three inputs high to produce a high
The OR gates had to have just one input high to produce a high output

## Slide 23: Multisim

## Slide 24: Troubleshooting:
Did not have any problems. If problems occurred could use multimeter to test circuit.

## Slide 25: Conclusion:
In this lab we used two input gates and wired them to another two input gate
To create a three input gate. They functioned in the same matter

## Slide 26: Data Sheets:

## Slide 30: Lab 2
By: Chad Creager
Lab Partner:
Instructor: A Bell
Class: EECT 122
Date: 9/14/15

## Slide 31: Objectives:
Design build and test a NAND gate latch

## Slide 32: Equipment and Parts:
Bench 3
HY1802D Power Supply
GWINSTEK Multi Meter Ser # CL860260
Bread Board
Dip Switches
2- 1KOHM Resistors
1- 74LS00
Wires
Oscilliscope

## Slide 33: Theories:

## Slide 34: Data/Lab Results/Simulations/Schematics:
The simulation does not work well in Multisim.
The real world example works better as long as you do not use the undefined situation.

## Slide 42: Multisim

## Slide 43: Troubleshooting:
The simulation did not work properly even put signal analyzer to try and check circuit.
Used Multimeter to test all input levels and output levels.
Tested output with a load and without.

## Slide 44: Conclusion:
The lab shows how a NAND gate works but also shows what happens when you have an undefined state. This is the second semester that have built this circuit and multisim does not operate correctly.

## Slide 45: Data Sheets:

## Slide 48: Lab 3
By: Chad Creager
Lab Partner:
Instructor: A Bell
Class: EECT 122
Date: 9/14/15

## Slide 49: Objectives:
Design, build and test a SR FF

## Slide 50: Equipment and Parts:
Bench 3
HY1802D Power Supply
GWINSTEK Multi Meter Ser # CL860260
Bread Board
Dip Switches
2- 1KOHM Resistors
1- 74LS02
Wires

## Slide 51: Theories:

## Slide 52: Data/Lab Results/Simulations/Schematics:
Sorry Andy no pictures my camera was dead

## Slide 53: Multisim

## Slide 54: Conclusion:
This lab works.
No picture of lab due to camera being dead.
This is very similar to the nand latch lab.

## Slide 55: Data Sheets:

## Slide 57: Lab 4
By: Chad Creager
Lab Partner:
Instructor: A Bell
Class: EECT 122
Date: 9/14/15

## Slide 58: Objectives:
Design, build and test a D FF

## Slide 59: Equipment and Parts:
Bench 3
HY1802D Power Supply
GWINSTEK Multi Meter Ser # CL860260
Bread Board
Dip Switches
3- 1KOHM Resistors
1- 74LS74
Function Generator
Wires

## Slide 60: Data/Lab Results/Simulations/Schematics:
No photos due to dead camera.

## Slide 61: Multisim

## Slide 62: Conclusion:
No photos of this lab.
This lab is very similar to the previous two labs.

## Slide 63: Data Sheets:

## Slide 66: Lab 5
By: Chad Creager
Lab Partner:
Instructor: A Bell
Class: EECT 122
Date: 9/14/15

## Slide 67: Objectives:
Design, build and test a JK FF

## Slide 68: Equipment and Parts:
Bench 3
HY1802D Power Supply
GWINSTEK Multi Meter Ser # CL860260
Bread Board
Dip Switches
4- 1KOHM Resistors
1- 74LS76
Function Generator
Wires

## Slide 69: Theories:

## Slide 70: Data/Lab Results/Simulations/Schematics:
Sorry Andy no photos camera was dead.

## Slide 71: Multisim

## Slide 72: Conclusion:
This lab is similar to previous lab just uses different type of gates.
No pics due to camera was dead at time of simulation.

## Slide 73: Data Sheets:

## Slide 74: Lab 6
By: Chad Creager
Lab Partner:
Instructor: A Bell
Class: EECT 122
Date: 9/14/15

## Slide 75: Objectives:
Simulated, built and test the 74LS283 2’s complement and 4 bit adder

## Slide 76: Equipment and Parts:
Bench 3
HY1802D Power Supply
GWINSTEK Multi Meter Ser # CL860260
Bread Board
Dip Switches
8- 1KOHM Resistors
1-
1 red LED
Wires

## Slide 77: Theories:

## Slide 78: Data/Lab Results/Simulations/Schematics:
Didn’t run in multisim was working on Lou’s board.

## Slide 80: Multisim

## Slide 81: Troubleshooting:
Had to change wiring to the led to get orientation correct.
Had to check orientation of wiring when first wired up.

## Slide 82: Conclusion:
Created two bit adder in both multisim and real life.
This was a test to keep all the wiring straight.

## Slide 83: Data Sheets:

## Slide 85: Lab 7
By: Chad Creager
Lab Partner:
Instructor: A Bell
Class: EECT 122
Date: 11/9/15

## Slide 86: Objectives:
Design, built and test a 4 counter (synchronous)

## Slide 87: Equipment and Parts:
Bench 3
HY1802D Power Supply
GWINSTEK Multi Meter Ser # CL860260
Bread Board
Frequency Generator
1- 74LS73, 74LS47, 74LS08
1 Green LED
Wires

## Slide 88: Theories:
The counter is synchronous because it is hooked to the same clock

## Slide 89: Data/Lab Results/Simulations/Schematics:

## Slide 91: Multisim

## Slide 92: Troubleshooting:
No problems but if I would have had problems could have used multimeter to check signals.
Had to rework algebra a couple of time to simplify better.

## Slide 93: Conclusion:
This counter worked well.
Was able to use this counter to test other labs.

## Slide 94: Data Sheets:

## Slide 99
Datasheet for 74LS73 is in Lab11
Datasheet for 74LS08 is in Lab 0

## Slide 100: Lab 8
By: Chad Creager
Lab Partner:
Instructor: A Bell
Class: EECT 122
Date: 10/12/15

## Slide 101: Objectives:
Design, built and test a Mod 12

## Slide 102: Equipment and Parts:
Bench 3
HY1802D Power Supply
GWINSTEK Multi Meter Ser # CL860260
Bread Board
2- 1KOHM Resistors
1- 74LS73, 74LS08, 74LS00
1 Green LED*4
Wires
Frequency Generator

## Slide 103: Theories:
That gates can be moved to adjust what the counters count to
Moved gate and made a mod 10 also which is considered a decade counter.

## Slide 104: Data/Lab Results/Simulations/Schematics:

## Slide 105: Multisim

## Slide 107: Troubleshooting:
No problems but if I would have had problems could have used multimeter to check signals.
Had to rework algebra a couple of time to simplify better.

## Slide 108: Conclusion:
Add 74LS08 to circuit to change type of counter.
Also made a mod 10 counter by moving chip.

## Slide 109: Data Sheets:
Datasheet for 74LS73 is in Lab 11
Datasheet for 74LS08 is in Lab 0
Datasheet for 74LS00 is in Lab 2

## Slide 110: Lab 9
By: Chad Creager
Lab Partner:
Instructor: A Bell
Class: EECT 122
Date: 10/19/15

## Slide 111: Objectives:
Boolean Reduction – simulation and simplification

## Slide 112: Equipment and Parts:
Bench 3
HY1802D Power Supply
GWINSTEK Multi Meter Ser # CL860260
Bread Board
Dip Switches
3- 1KOHM Resistors
1- 74LS08N, 74LS32, 74LS04
1 Green LED
Wires

## Slide 113: Theories:

## Slide 114: Data/Lab Results/Simulations/Schematics:
Built both circuits simplified and original circuit.

## Slide 116: Multisim

## Slide 117: Troubleshooting:
No problems but if I would have had problems could have used multimeter to check signals.
Had to rework algebra a couple of time to simplify better.

## Slide 118: Conclusion:
With the use of K-maps and algebra I was able to reduce the Boolean equation.
Used algebra first and had to try it a couple of different ways to get the equation simplified.

## Slide 119: Data Sheets:

## Slide 126
Datasheet for 74LS32 is in Lab 1
Datasheet for 74LS08 is in Lab 0
Datasheet for 74LS00 is in Lab 2

## Slide 127: Lab 10
By: Chad Creager
Lab Partner:
Instructor: A Bell
Class: EECT 122
Date: 9/14/15

## Slide 128: Objectives:
74185 Model development

## Slide 129: Equipment and Parts:
Bench 3
Multisim

## Slide 130: Theories:
Use multisim to develop a 74185 IC that is obsolete.

## Slide 131: Data/Lab Results/Simulations/Schematics:
Data table for 74185
Example below is a
Modified IC so that
Will display count in Hex
Correctly.

## Slide 132: Multisim

## Slide 134: Troubleshooting:
Had to check the programming a couple of times.

## Slide 135: Conclusion:
Created the 74185 IC in multisim. No way to test IC without putting the logic in programmable IC.

## Slide 136: Data Sheets:
This data sheet is located in Lab FF

## Slide 137: Lab 11
By: Chad Creager
Lab Partner:
Instructor: A Bell
Class: EECT 122
Date: 10/19/15

## Slide 138: Objectives:
Binary to 7 segment display

## Slide 139: Equipment and Parts:
Bench 3
HY1802D Power Supply
GWINSTEK Multi Meter Ser # CL860260
Bread Board
Dip Switches
2- 1KOHM Resistors
1- 74LS73
7 segment display
Wires

## Slide 140: Theories:
Trying to use IC’s to convert a binary signal to a 7 segment display.
No IC is available to do this in Hexadecimal
It can be done with a programmable IC.

## Slide 141: Data/Lab Results/Simulations/Schematics:
When running the circuit it performed exactly like the data sheet said it would.

## Slide 142: Multisim

## Slide 144: Troubleshooting:
The current IC’s available wouldn’t count in Hexadecimal or display.
Had to change set-up of IC in multisim to accomplish this.

## Slide 145: Conclusion:
This lab is a good example of how programmable IC’s can simplify a circuit and also do what you can’t with other IC’s

## Slide 146: Data Sheets:

## Slide 148: Lab 12
By: Chad Creager
Lab Partner:
Instructor: A Bell
Class: EECT 122
Date: 11/30/15

## Slide 149: Objectives:
Xilinx CPLD effort

## Slide 150: Equipment and Parts:
Bench 3
Xilinx Lab Kit

## Slide 151: Theories:
Using Xilinx to create a circuit.
This eliminates some of the IC chips needed

## Slide 152: Data/Lab Results/Simulations/Schematics:
Used Programming software to create a program to simplify the circuit.

## Slide 154: Program
Didn’t take a picture of the program and can’t load the program from laptop.

## Slide 155: Troubleshooting:
Where to begin? The biggest problem with this lab was that couldn’t download the program to the microproccesser.
I tried this on a couple of occasions and never got it to work.
Tried all port configurations but nothing worked.

## Slide 156: Conclusion:
The Xilinx lab was frustrating for a couple of reasons.
The programming was different and sometimes difficult to interpret.
Couldn’t get the program downloaded once I had it figured out.

## Slide 157: Data Sheets:
http://www.xilinx.com/support/documentation/data_sheets/ds312.pdf
The Data sheet is massive so just supplied a link

## Slide 158: Lab 13
By: Chad Creager
Lab Partner:
Instructor: A Bell
Class: EECT 122
Date: 11/30/15

## Slide 159: Objectives:
Arduino Labs

## Slide 160: Equipment and Parts:
Bench 3
Arduino Lab Kit

## Slide 161: Theories:
Using Arduino’s to create a circuit.
This eliminates some of the IC chips needed

## Slide 162: Data/Lab Results/Simulations/Schematics:
Build three individual labs to show how microprocessor simplifies circuit
First lab was using a switch to change LED’s
Second lab was showing temperature to change LED’s
Third lab was making a magic 8-ball that changed when you shake circuit board

## Slide 163: PROGRAM

## Slide 168: Troubleshooting:
The labs were pretty straightforward the only issue was that the tilt switch wanted to keep falling out on the magic 8-ball.

## Slide 169: Conclusion:
The Arduino is one way to make a complicated IC circuit smaller with the use of a microproccessor.

## Slide 170: Data Sheets:

## Slide 172: Lab 14
By: Chad Creager
Lab Partner:
Instructor: A Bell
Class: EECT 122
Date: 12/7/15

## Slide 173: Objectives:
Arduino Labs Part 2

## Slide 174: Equipment and Parts:
Bench 3
Arduino Lab Kit

## Slide 175: Theories:
Using Arduino’s to create a circuit.
This eliminates some of the IC chips needed

## Slide 176: Data/Lab Results/Simulations/Schematics:
Built a circuit and programmed microproccesor so that when a potentiometer
was turned the servo followed suit.

## Slide 178: program

## Slide 179: Troubleshooting:
When I first assembled circuit the servo would shake.
To correct this problem I had to install capacitors to clean up signals.

## Slide 180: Conclusion:
The Arduino is one way to make a complicated IC circuit smaller with the use of a moicroproccessor.

## Slide 181: Data Sheets:

## Slide 183: Lab FF
By: Chad Creager
Lab Partner:
Instructor: A Bell
Class: EECT 122
Date: 11/2/15

## Slide 184: Objectives:
Develop a schematic for Lou’s box

## Slide 185: Equipment and Parts:
Bench 3
Multisim
Multimeter

## Slide 186: Theories:
This circuit uses many of the Theroms located in the cover of the book

## Slide 187: Data/Lab Results/Simulations/Schematics:
Worked on creating a chip and figuring out Lou’s adder.
Did not get whole circuit completed

## Slide 189: Multisim

## Slide 197: Troubleshooting:
I did not do much troubleshooting since didn’t finish schematic.
One type of testing I had to do was to use a meter to test continuity on Lou’s board to determine where some of the wires went.

## Slide 198: Conclusion:
The 74LS185 is obsolete and I think it is so that we don’t have to try and build things like this.
The 74ls185 had to be made using a data sheet.

## Slide 199: Data Sheets: