## Slide 1: Lab 8 JFET Transistor Amplifier Circuit
By: Dakota Johnson
Lab Partner: Sue Hlaing, Josiah Abel
Instructor: Andy Bell
Bench Number: 6
Class: EECT 121-50C
Date: 12/15/2015

## Slide 2: Objectives:
Build a circuit using N-Type JFET that produces a voltage gain of 10.
Equipment and Parts:
    Oscilloscope Brand: Tektronix Model #: TDS220 SN: B083266
    Digital Multi Meter Brand: GwInstek Model #: GDM-8245 SN: CL860332
    Function Generator Brand: GwInstek Model #: GFG-8210 SN: C705245
    GW Instek LCR meter model#: LCR-819 SN#: E120998
    DC Power Supply Model# HY1802D

## Slide 3: Data/Lab Results/Simulations/Schematics:
.model 2N5457DHJ NJF(Vto=-1.372 Beta=1.125m Lambda=2.3m
+ Vtotc=-2.5m Is=181.3f Isr=1.747p N=1 Nr=2 Xti=3 Alpha=2.543u
+ Vk=152.2 Cgd=4p M=.3114 Pb=.5 Fc=.5 Cgs=4.627p Kf=10.45E-18
+ Betatce=-.5 Rd=1 Rs=1 Af=1)
Model of 2N5457 used in the simulations
Multisim Schematics of the circuit.

## Slide 4
 | Measured | Expected | 
V1 | -5.071 | -5 | V
V2 | 9.043 | 9 | V
Vin | 24.8 | 5 | mV Pk-Pk
Freq | 1 | 1 | kHz
C1 | 1.01 | 1 | μF
C2 | 0.948 | 1 | μF
R1 | 4.67 | 4.7 | kΩ
R2 | 32.6 | 33 | kΩ
R3 | 21.98 | 22 | kΩ
R4 | 32.89 | 33 | kΩ
Vout | 240 | 5.88 | mV Pk-Pk
β | 9.677419 | 1.176 | 
1μF Capacitor
2N5457 N-Type JFET Transistor
4.7kΩ Resistor
33kΩ Resistor
33kΩ Resistor
22kΩ Resistor
Function generator settings
Oscilloscope reading of input and output voltage

## Slide 5: Troubleshooting:
  The first simulation was working correctly but when the circuit was built in the lab with the simulations specifications the gain was only 3. The circuit was fixed by changing resistors R3 and R4 until a gain of 10 was achieved. This set up was then simulated and it was concluded that the part model used did not represent the actual part fully.

## Slide 6: Conclusion:
The circuit was able to produce a voltage gain of 10.

## Slide 7: Data Sheets:
2N5457 N-Type Transistor