## Slide 1: Lab 8
By: Dakota Johnson
Lab Partner: Josiah Abel
Instructor: Andy Bell
Bench Number: 6
Class: EECT 122-20C
Date:3/18/2015

## Slide 2: Objectives:
To build an asynchronous counting circuit and to find the total propagation delay in the circuit.
Equipment and Parts:
Equipment | Model/Part Number | Serial Number
NI Elvis II+ | 19857OA-02L | 1677D1E
Digital Multimeter | GW INSTEK GDM-8245 | CL860332
Tektronix TDs 220 2-Channel Ocilloscope | TDS220 | B083266
Function Generator | GW INSTEK GFG -8210 | C705245
Part | Amount
330 Resistors | 4
74LS112D Chip | 2
74LS04D Chip | 1
LED 08LX330HV5 | 4
Miscellaneous Wires | ------------

## Slide 3: Data/Lab Results/Simulations/Schematics:
Simulation showing the timing of the outputs with respect to the clock.
Simulation of total propagation delay.

## Slide 4
Output Voltages |  | 
 | High Voltage | Low Voltage
 | (V) | (V)
MSB | 3.846 | 0.102
3rd Bit | 3.84 | 0.121
2nd Bit | 3.85 | 0.13
LSB | 3.85 | 0.12
Total Propagation Delay
Time
(ns)
52
Clock Frequency
Frequency
(kHz)
1.08
74LS112
74LS04
330 Resistors

## Slide 5: Troubleshooting:
  When the circuit was first tested it was counting in an erratic pattern.
    The issue was dealt with by looking over the circuit. It was found that a wire had not be placed on the right pin which resulted in the circuit’s odd counting. Once the wire was placed on the correct pin the circuit worked correctly.

## Slide 6: Conclusion:
The circuit was constructed and the propagation delay was found to be 52ns.

## Slide 7: Data Sheets:
74LS112
74LS04