## Slide 1
Class and Lab Notebook
ECTT 112
Spring 2014
Douglas Villeda

## Slide 2: LAB 1
OR & AND Gates
Purpose: Learn how to set up and test OR and AND gates.

## Slide 3: OR Gate- multisim with true table
A | B | Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 4: OR Gate Lab- Material
74LS32P – GATE -1
DIP SWITCH -1
10k OHMS RESISTORS -2
NI Elvis II

## Slide 5
SET UP
This is a low and low
This is a low and high

## Slide 6: AND GATE –multisim and true table
C | D | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 7: LAB MATERIAL
74LS08P – OR GATE 1
DIP SWITCH 1
10k OHMS RESISTORS 2
NI Elvis II

## Slide 8
SET UP
This is and high and high

## Slide 9: Conclusion
THE DIP SWITCH WAS VERY HELPFUL WITH THE SET UP AND THE VISUALIZATION OF THE TEST. WE WERE ABLE TO TEST OF POSIBILITIES OF THE INPUTS.

## Slide 10: Nand Gate
Building a circuit with Nand’s gates only

## Slide 11: Original circuit
Objective: Build this circuit using only NAND gates.

## Slide 12: Brute force method
This method uses too many NAND gates
Double Inversion can be eliminated!!!!!

## Slide 13: NAND gates
This is helpful because you use only four NAND gates instead of twelve.
8 NAND gates were eliminated. They were double Inverters.

## Slide 14: True table
 | A | B | C | D | A' | B' | C' | D' | A'+B | C'+D' | (A'+B')(C'+D') | 
 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 
 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 
 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 
 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 
 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 
 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 
 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 
 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 
 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 
 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 
 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 
 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 
 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 
 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 
 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 
 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 

## Slide 15: LAB 2
EQUIVALENT CIRCUITS– NANDS AND NORS
  Materials
    Gates: 74LS04, 74LS32, 74LS08
    10k Ohms REISTORS: 4
    DIP SWITCH: 1
    NI ELVIS ll
    DMM

## Slide 16
Build the following circuits in the lab.

## Slide 17: NAND GATES ONLY CIRCUIT.
This circuit has been reduced due to the use of only NAND gates and has the same results than the original.

## Slide 18: Truth table
 | A | B | C | D | A' | B' | C' | D' | A'+B | C'+D' | (A'+B')(C'+D') | 
 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 
 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 
 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 
 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 
 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 
 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 
 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 
 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 
 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 
 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 
 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 
 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 
 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 
 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 
 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 
 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 

## Slide 19: Led “1” with dmm

## Slide 20: Led “0” with dmm

## Slide 21: Original circuit
Build this circuit and test it

## Slide 22: Led “1” with dmm

## Slide 23: Led “0” with dmm

## Slide 24: conclusion
This was a very interesting lab because the the difference between the two circuits, using I chip vs 3, and the high “1’” with DMM was not exactly 5V because the LED voltage drop.

## Slide 25: Mid term Circuit
500nv = low . This is a multisim error.

## Slide 26: Circuit with one chip only

## Slide 27: Lab original 3 chips

## Slide 28: Lab – 1 chip

## Slide 29: D-flip flop multisim

## Slide 30: D-flip flop with clock

## Slide 31: Basic Stamp Lab 1
Start learning some basic of basic stamp and programing

## Slide 32: The program

## Slide 33: Lab set up

## Slide 34: The Push bottom is pressed

## Slide 35: Basic Stamp 2

## Slide 36: program

## Slide 41: Basic stamp Binary counter

## Slide 42: Program -set up

## Slide 43: Main Code
It flashes all the LEDs before and after the mail program

## Slide 44: Subroutines

## Slide 45: Lab Video
LED failure