## Slide 1: EECT 121 Lab Notebook
ELECTRONIC PROJECTS
Spring 2015
Ken Fischer
Eh Doh Lwe
5-5-15

## Slide 2: Table of Contents
Diode 3
Diode Rectifier 7
Bipolar Junction Transistors 10
BJT Amplifier Circuits 14
Field-Effect Transistors and Circuits 17
Operation Amplifier 19
Oscillator 23
Silicon-Controlled Rectifier (SCR) 26

## Slide 3: Diode

## Slide 4: Diode
Objective
    To understand how diode works.
Equipment and Material
    Function Generator, Oscilloscope, various diode, and 1k resistors
Research and Information
  https://www.youtube.com/watch?v=OyC02DWq3mI

## Slide 5: Diode Details

## Slide 6: Diode
Summary and Conclusion
Biased in one direction
Voltage drop of .7v
Reverse breakdown voltage
The diode is like a water check valve. The source
only passes in one direction but still takes
certain minimum amount of voltage to achieve this which is call the forward biased of the diode.
The source voltage flows into the
anode out through the cathode.

## Slide 7: Diode Rectifier (created half wave)
Convert AC power source to DC

## Slide 8: Bridge Rectifier
AC input
Output
Output

## Slide 9: Summary
Our desire result was the graph on the left , our real result was actually on the right. We were sure that we applied voltage input correctly and measure output correctly. This may have been from not adjusting the oscilloscope correctly. We did learned overall how the bridge rectifier should operate. It passes through two diodes with one polarity and then through two different diodes when the polarity is reversed, outputting a constant wave.

## Slide 10: Bipolar Junction Transistors
Objective
  To understand how a transistor operate
Equipment and Material
    DMM,2N3904 transistor, (2) 10k resistors, 1k resistor, 470ohm resistor, and Elvis
Research and Information
  Youtube video and book

## Slide 11: Mathematically
PHTSICAL EXPERIMENT RESULTS
5 VOLT SOURCE DIVIDED BY 20 OHMS MATHMATICALLY
RESULTS .25mA
Actually result was 250 uA
VR2= 10k*.25uA= 2.5V (actual 2.4177v)
VRE= 2.5V-.7V= 1.8V (actual 1.78v)
IRE=1.8V/1k=1.8mA
VRC= 470K*1.58mA=.846V (actual .8305V)
VCE=VCC-VRC=2.354V (actual 2.3072v)
VR2
VRE
IRE
VRC

## Slide 12: Book examples BJT – NPN Transistor in multisim (Open/Close)

## Slide 13: Conclusion
The outputs of voltage and amperage applied and measure to the transistor operated almost identical to what we had predicted.
The two 10k ohm resistor acted as a voltage divider input into the base of a transistor. The results of this 2.5v impression on the transistor was measured at different point.

## Slide 14: BJT Amplifier Circuits
Objective
  To look at different amplifier configurations and recognize the gain outputs created from the different inputs.

## Slide 15: Schematic for current gain type Amp

## Slide 16: Conclusion
Different type of setup produce different output result
The capacitors are recognized as being very important in the amplifier circuit.
There was phase reversal from the input to the output.

## Slide 17: Field-Effect Transistors and Circuits
Objective
  Comparing the field effect transistor to the BJT
BJT
Field Effect Transistors

## Slide 18: Conclusion
Though the JFET is similar to the BJT, they operate almost opposite.
In BJT, increase in base input result in lower resistance where in JFET, increase input to the gate will eventually pinch-off the JFET.

## Slide 19: Operation Amplifier

## Slide 20: inverting
Rf
Ri
Input signal applied to inverting input through Ri and the inverted output feeds by through Rf.
The negative sign indicated the output is inverted from the input signal.
Positive grounded equal the value of the input signal.
Equation:
Av = - (Rf/Ri)

## Slide 21: Non-inverting
The junction of the feedback resistor (Rf) and the input resistor (Ri) are still on the negative terminal.
Equation:
Av = (Rf/Ri) + 1

## Slide 22: Summary and Conclusion
The inverting amplifier use the negative terminal for the source input and the positive terminal as a ground. Conversely, the non-inverting uses the positive terminal as the source input but the Rf and Ri are still connected in the same negative terminal.
Both amplifier are similar in that they both have a voltage gain at the output though it may be positive/negative.

## Slide 23: Oscillator

## Slide 24: schematic

## Slide 25: Good YouTube videos we found
With function generator
Without function generator

## Slide 26: Silicon-Controlled Rectifier (SCR)

## Slide 27: Schematic

## Slide 28: Summary and Conclusion
These devices need a main source to operate but are actually activated by very minimum input.