## Slide 1: EECT 111 Lab Notebook
Intro to Circuit Analysis
Fall 20015
By: Ivan Cervantes
12-17-15

## Slide 2: Table of Contents
Lab 1 – Resistor Variability 4
Lab 2 – Reading and Sorting Resistors 10
Lab 3 – Series Resistors 14
Lab 4 – Black Box Design 1 20
Lab 5 – MEMS Variable Resistor 26
Lab 6 – Black Box Design 2 27
Lab 7 – 4 Resistor Parallel Circuit 33

## Slide 3: Table of Contents Cont.
Lab 8 – Black Box Design 3 39
Lab 9 – Series/Parallel Resistors 45
Lab 10 – Series/Parallel Capacitors 54
Lab 11 – RC Lab 60
Lab 12 – Series/Parallel Inductors 66
Lab 13 – RL Lab 73
Other Work 80

## Slide 4: Lab 1 – Resistor Variability

## Slide 5: Lab 1 – Resistor Variability
Objective
  To gather 20 resistors of the exact same value, put them on a breadboard, and measure the individual resistances.
Equipment and Material
  Jumper wires, 20 470 ohm resistors, Digital Multimeter, and breadboard

## Slide 6: Lab 1 – Resistor Variability
Procedure
Collected the materials and equipment needed
Measured each individual resistor using the Multimeter
Recorded the results in an excel spreadsheet and graphed the results

## Slide 7: Lab 1 – Resistor Variability

## Slide 8: Lab 1 – Resistor Variability
0.4638 | k ohm
0.4584 | k ohm
0.4661 | k ohm
0.4548 | k ohm
0.4569 | k ohm
0.4592 | k ohm
0.4622 | k ohm
0.4625 | k ohm
0.4589 | k ohm
0.4625 | k ohm
0.4607 | k ohm
0.4615 | k ohm
0.4563 | k ohm
0.4626 | k ohm
0.4621 | k ohm
0.4569 | k ohm
0.464 | k ohm
0.4613 | k ohm
0.4582 | k ohm
0.4524 | k ohm
0.4524 | min
0.4661 | max
0.460065 | ave
0.003448 | STDEV
Chart: 
 | 0.4638 | 0.4584 | 0.4661 | 0.4548 | 0.4569 | 0.4592 | 0.4622 | 0.4625 | 0.4589 | 0.4625 | 0.4607 | 0.4615 | 0.4563 | 0.4626 | 0.4621 | 0.4569 | 0.464 | 0.4613 | 0.4582 | 0.4524

## Slide 9: Lab 1 – Resistor Variability
Summary
  No Multisim was used for the lab. I learned how to measure resistance using a multimeter and that resistor values are not exact, but have an accepted percent error that determines whether should be used for accurate results.

## Slide 10: Lab 2 – Reading and Sorting Resistors

## Slide 11: Lab 2 – Reading and Sorting Resistors
Objective
  Measured resistance and learn how to determine resistor values based on color codes.
Equipment and Material
  Jumper wires, Digital Multimeter, and breadboard, Resistors: 100 ohms, 220 ohms, 470 ohms, 1 kohms, 2.2 kohms, 3.3 kohms, 4.7 kohms, 10 kohms, 47 kohms, 100 kohms, 1 Mohms, 10 Mohms

## Slide 12: Lab 2 – Reading and Sorting Resistors
Procedure
Gathered all of the materials required for the lab
Hooked up each individual resistor to the breadboard
Measured each individual resistor and recorded the data on the lab sheet

## Slide 13: Lab 2 – Reading and Sorting Resistors

## Slide 14
Summary
  No Multisim was used for the lab. I learned how to determine the value of individual resistors by examining their colors using the resistor color code. I also used the digital mustimeter to confirm the values.
Lab 2 – Reading and Sorting Resistors

## Slide 15: Lab 3 – Series Resistors

## Slide 16: Lab 3 – Series Resistors
Objective
  Lean how to measure resistors when connected in series and learn how to measure current, voltage, and voltage at specific points on the circuit.
Equipment and Material
  Jumper wires, DC Power Output, Digital Multimeter, and breadboard, Resistors: 10 kohms, 2.2 kohms, and 4.7 kohms.

## Slide 17: Lab 3 – Series Resistors
Procedure
Created a multisim simulation
Created an excel file with calculations for total resitance, voltage drops, and current.
Collected the materials and equipment needed
Hooked up each individual resistor in a series circuit layout
Measured the individual resistor and the total resistance in a series circuit layout using the multimeter
Recorded the data on the lab sheet
Added power to the series circuit
Used the multimeter to measure voltage at specific points, output voltage, and current
Recorded the data on the lab sheet

## Slide 18: Lab 3 – Series Resistors

## Slide 19: Lab 3 – Series Resistors
 | Values | 
R1 = | 10.0E+3 | Ω
R2 = | 2.2E+3 | Ω
R3 = | 4.7E+3 | Ω
RT = | 16.9E+3 | Ω
 | Values | 
IT = | 532.5E-6 | A
V1 = | 9 | V
VA = | 3.7E+0 | V
VB = | 2.5E+0 | V

## Slide 20
Summary
  I used Mulitsim to design a schematic that measured total resistance, total voltage, voltage A, voltage B, and current. Then I calculated total resistance, total voltage, voltage A, voltage B, and current. I compared my calculations results to my Mulitsim results and found them to be fairly accurate. I then learned how to use the multimeter to measure the voltage at a specific point on the circuit, the current, and the total resistance.
Lab 3 – Series Resistors

## Slide 21: Lab 4 – Black Box Design 1

## Slide 22: Lab 4 – Black Box Design 1
Objective
  The objective of this lab was to determine the value of the three resistors located in the black box using only the information provided in an image. The application of ohms law was the key.
Equipment and Material
  Jumper wires, Digital Multimeter, breadboard, DC Power Output, Resistors: 470 ohms, 330 ohms, 100 ohms

## Slide 23: Lab 4 – Black Box Design 1
Procedure
Create a current vs. resistance graph in excel to easily pick out resistors
Create a multisim simulation to check our work
Gather the necessary materials to build the circuit
Measure output voltage, total current, individual resistors, and total resistance using the multi meter
Record data on lab sheet

## Slide 24: Lab 4 – Black Box Design 1

## Slide 25: Lab 4 – Black Box Design 1
Chart: Current vs Resistance
| 90.000000000000398 | 122.4000000000004 | 154.80000000000041 | 187.20000000000041 | 219.60000000000042 | 252.00000000000043 | 284.40000000000043 | 316.80000000000041 | 349.20000000000039 | 381.60000000000036 | 414.00000000000034 | 446.40000000000032 | 478.8000000000003 | 511.20000000000027 | 543.60000000000025 | 576.00000000000023 | 608.4000000000002 | 640.80000000000018 | 673.20000000000016 | 705.60000000000014 | 738.00000000000011 | 770.40000000000009 | 802.80000000000007 | 835.2 | 867.6 | 900 | 1224 | 1548 | 1872 | 2196 | 2520 | 2844 | 3168 | 3492 | 3816 | 4140 | 4464 | 4788 | 5112 | 5436 | 5760 | 6084 | 6408 | 6732 | 7056 | 7380 | 7704 | 8028 | 8352 | 8676 | 9000
 | 0.1 | 0.073529 | 0.05814 | 0.048077 | 0.040984 | 0.035714 | 0.031646 | 0.028409 | 0.025773 | 0.023585 | 0.021739 | 0.020161 | 0.018797 | 0.017606 | 0.016556 | 0.015625 | 0.014793 | 0.014045 | 0.013369 | 0.012755 | 0.012195 | 0.011682 | 0.011211 | 0.010776 | 0.010373 | 0.01 | 0.0073529 | 0.005814 | 0.0048077 | 0.0040984 | 0.0035714 | 0.0031646 | 0.0028409 | 0.0025773 | 0.0023585 | 0.0021739 | 0.0020161 | 0.0018797 | 0.0017606 | 0.0016556 | 0.0015625 | 0.0014793 | 0.0014045 | 0.0013369 | 0.0012755 | 0.0012195 | 0.0011682 | 0.0011211 | 0.0010776 | 0.0010373 | 0.001

## Slide 26
Summary
  In this lab I learned how to apply ohms law in order to calculate total resistance when only given the current and voltage. I also learned the relationship between current and resistance through the graph created in excel. I now know how to use a digital multimeter at a basic level and have a firmer understanding of series circuits.
Lab 4 – Black Box Design 1

## Slide 27: Lab 5 – MEMS Variable Resistor
Error 404 Lab not found

## Slide 28: Lab 6 – Black Box Design 2

## Slide 29: Lab 6 – Black Box Design 2
Objective
  The objective of the lab was to determine which resistors were required to be wired in series to achieve the current displayed in the picture. It was also required to do the same in parallel.
Equipment and Material
  Jumper wires, Digital Multimeter, breadboard, DC Power Output, Resistors: 550ohms, 330 ohms, 220 ohms, 1 kohm, 1 kohm

## Slide 30: Lab 6 – Black Box Design 2
Procedure
Created a multisim simulation to easily determine the resistors needed
Created a excel spreadsheet to calculate which resistors are needed
Gather the necessary materials to build the circuit
Placed the resistors in series format
Measured the current and it turned out to be close enough
Record data on lab sheet
Redesigned the circuit to be a parallel circuit
Measured the current and received the correct data
Recorded data to lab sheet

## Slide 31: Lab 6 – Black Box Design 2

## Slide 32: Lab 6 – Black Box Design 2
 | Values | 
V1 = | 9 | V
IT = | 18.0E-3 | A
RT = | 500 | Ω
R1 = | 250 | Ω
R2 = | 250 | Ω
 | Values | 
V1 = | 9 | V
IT = | 18.0E-3 | A
RT = | 500 | Ω
R1 = | 1.0E+3 | Ω
R2 = | 1.0E+3 | Ω

## Slide 33
Summary
  In this lab I learned how to apply ohms law in order to calculate total resistance when only given the current and voltage. The difference between the lab 4 was that we did it both in parallel and series. The only major difference was the wiring and the calculation of the total resistance. The calculation for current stayed the same.
Lab 6 – Black Box Design 2

## Slide 34: Lab 7 – 4 Resistor Parallel Circuit

## Slide 35: Lab 7 – Resistor Parallel Circuit
Objective
  The objective of this lab was to build a parallel circuit using predetermined resistors and to measure the total current and the specific current at certain points on the circuit.
Equipment and Material
  Jumper wires, Digital Multimeter, breadboard, DC Power Output, Resistors: 2.2 kohm, 3.3 kohm, 4.7 kohm, 4.7 kohm.

## Slide 36: Lab 7 – Resistor Parallel Circuit
Procedure
Created a multisim simulation to find the current at certain points on the circuit and to find the total resistance
Created a excel spreadsheet to calculate current at certain points on the circuit and to calculate the total resistance
Gather the necessary materials to build the circuit
Placed the resistors in a parallel format and ran power through them
Found the actual value of the resistors by using the multi meter
Measured the current with the multimeter on different points on the parallel circuit
Record data on lab sheet

## Slide 37: Lab 7 – Resistor Parallel Circuit

## Slide 38: Lab 7 – Resistor Parallel Circuit
 | Values | 
R1 = | 2.2E+3 | Ω
R2 = | 3.3E+3 | Ω
R3 = | 4.7E+3 | Ω
R4 = | 4.7E+3 | Ω
 | Values | 
V1 = | 9 | V
RT = | 845.23 | Ω
I1 = | 4.1E-3 | A
I2 = | 2.7E-3 | A
I3 = | 1.9E-3 | A
I4 = | 1.9E-3 | A
IT = | 10.6E-3 | A

## Slide 39
Summary
  In this lab I practiced measuring current on a parallel circuit. Calculating total resistance in a parallel circuit poses no trouble for me at this point. I learned that current on a parallel circuit depends on the resistor before or after the point that is being used to measure current.
Lab 7 – Resistor Parallel Circuit

## Slide 40: Lab 8 – Black Box Design 3

## Slide 41: Lab 8 – Black Box Design 3
Objective
  The objective of this lab was to determine what the value of the three resistors located in black box. We were also supposed to figure out whether they were in parallel or in series. After that, we had to adjust the first resistor to multimeter placed on circuit equal 1.3 volts
Equipment and Material
  Jumper wires, Digital Multimeter, breadboard, DC Power Output, Resistors: 5 4.7 ohm resistors and an adjustable 10k resistor.

## Slide 42: Lab 8 – Black Box Design 3
Procedure
Created a multisim simulation to find the value and format of the 3 resistors and to find the required adjustment for R1 to make the multimeter output 1.3 volts.
Created a excel spreadsheet to calculate the change in volts when we adjusted the R1
Gather the necessary materials to build the circuit
Placed the resistors in a series-parallel format and ran power through them
Found the actual value of the resistors by measuring them with the multimeter
Measured the voltage like it was displayed on the image to insure the output was correct
Replaced R1 with an adjustable resistor to make the output voltage 1.3 volts
Recorded the data on the lab sheet.

## Slide 43: Lab 8 – Black Box Design 3

## Slide 44: Lab 8 – Black Box Design 3
R (black Box) = | 1.6E+3 | Ω
 | Values | 
R1 = | 4.7E+3 | Ω
R2 = | 4.7E+3 | Ω
R3 = | 4.7E+3 | Ω
R4 = | 4.7E+3 | Ω
R5 = | 4.7E+3 | Ω
R1 (adjusted) = | 4.6E+3 | Ω
 | Values | 
V1 = | 9 | V
VA = | 5.14 | V
VB = | 3.86 | V
VA - VB = | 1.28 | V
VA (adj) = | 5.2 | V
VB (adj) = | 3.9 | V
VA - VB (adj) = | 1.3 | V

## Slide 45
Summary
  In this lab I applied what I had learned about resistors to determine the value of the resistors located in the box using only the information provided to me by the picture. After I figured out the values I then learned to use and adjustable resistor to make the output voltage on the multimeter 1.3 volts. It was confusing to adjust the resistor, but I soon understood how to do it. It was just a matter of carefully placing it in the right direction and fine-tuning it.
Lab 8 – Black Box Design 3

## Slide 46: Lab 9 – Series/Parallel Resistors

## Slide 47: Lab 9 – Series/Parallel Resistors
Objective
  The objective of this lab was to test us on all that we had learned in the previous eight class sessions.
Equipment and Material
  Jumper wires, Digital Multimeter, breadboard, DC Power Output, Resistors: 2 470 ohm, 2 1 kohm, 2.2 kohm, 3.3 kohm, 4.7 kohm, 10 kohm, adjustable resistor

## Slide 48: Lab 9 – Series/Parallel Resistors
Procedure
Created a multisim simulation to insure that I was competent enough to begin the lab
Created a excel spreadsheet to work on the calculations
Gather the necessary materials to build the circuit
Placed the resistors in a series-parallel format and measured the individual, grouped, and total resistance.
I then applied 9 volts of power to the circuit in order to calculate the voltage and current at certain points
Recorded the data on the lab sheet.

## Slide 49: Lab 9 – Series/Parallel Resistors

## Slide 50: Lab 9 – Series/Parallel Resistors

## Slide 51: Lab 9 – Series/Parallel Resistors
R1 = | 470
R2 = | 470
R3 = | 1.0E+3
R4 = | 1.0E+3
R5 = | 2.2E+3
R6 = | 3.3E+3
R7 = | 4.7E+3
R8 = | 10.0E+3
R34 = | 500
R567 = | 1030.565
R345678 = | 11530.565
R2345678 = | 451.593
RT = | 921.593

## Slide 52: Lab 9 – Series/Parallel Resistors
 | Power
VT = | 9
VA = | 4.410
VB = | 4.12
VC = | -1.06419
 | Current
IT = | 0.009766
IT = | 0.00957

## Slide 53: Lab 9 – Series/Parallel Resistors
 | Current
IT = | 0.009766
IT = | 0.00957
 | Power
VT = | 9
VA = | 4.410
VB = | 4.12
VC = | -1.06419

## Slide 54
Summary
  In this lab I applied what I had learned about in the previous eight weeks in order to complete the three tasks given to me. I had a strong start, but once I began to calculate voltages , I fell behind. I was able to do the simulations and measurements adequately enough, but fell short in the calculations portion
Lab 9 – Series/Parallel Resistors

## Slide 55: Lab 10 – Series/Parallel Capacitors

## Slide 56: Lab 10 – Series/Parallel Capacitors
Objective
  The objective of this lab was to teach us how capacitors act in a parallel and series format.
Equipment and Material
  Jumper wires, Digital Multimeter, breadboard, AC Power Output, LCR meter, Capacitors: 10 uF, 22 uF, 47, uF.

## Slide 57: Lab 10 – Series/Parallel Capacitors
Procedure
Created a multisim circuit, but I was not able to measure capacitance due to the lack of an LCR meter in the program
Gather the necessary materials to build the circuit
Placed the capacitors in a series format and measured the individual and total capacitance
Recorded the data on the lab sheet
Placed the capacitors in a parallel format and measured the individual and total capacitance
Recorded the data on the lab sheet

## Slide 58: Lab 10 – Series/Parallel Capacitors

## Slide 59: Lab 10 – Series/Parallel Capacitors

## Slide 60
Summary
  Calculating the capacitance of capacitors in a series format uses the same formula as calculating the resistance of resistors in a parallel format. It is the same scenario for calculating the capacitance of capacitors in a parallel format.
Lab 10 – Series/Parallel Capacitors

## Slide 61: Lab 11 – RC Lab

## Slide 62: Lab 11 – RC Lab
Objective
  The objective of this lab was to measure and record the value of specific capacitors using the LCR meter. After that we are to change the frequency and observe how it impacts the voltage.
Equipment and Material
  Jumper wires, Digital Multimeter, breadboard, Function Generator, Ocilloscope, LCR meter, Capacitors: 0.47 uF, 2.2 uF, 1 uF, Resistors: 1 kohm.

## Slide 63: Lab 11 – RC Lab
Procedure
Created a multisim circuit to simulate the lab
Gather the necessary materials to build the circuit
Built the circuit and measured the capacitance of each capacitor when they were implemented into the circuit
Recorded the data on the lab sheet
Had partner change the frequency while I recorded the output voltage on the lab sheet

## Slide 64: Lab 11 – RC Lab

## Slide 65: Lab 11 – RC Lab

## Slide 66
Summary
  We measured capacitance using and LCR meter and resistance using a multimeter. By adjusting the frequency on the function generator we were able to record the different output voltages for each capacitor used.
Lab 11 – RC Lab

## Slide 67: Lab 12 – Series/Parallel Inductors

## Slide 68: Lab 12 – Series/Parallel Inductors
Objective
  The objective of this lab was to measure and record the value inductors when put in a series circuit and a parallel circuit.
Equipment and Material
  Jumper wires, Digital Multimeter, breadboard, Function Generator, LCR meter, Inductors: 1 mH, 2.2 mH, 4.7 mH, Resistors: 1E-3 ohm.

## Slide 69: Lab 12 – Series/Parallel Inductors
Procedure
Created a multisim circuit to simulate the lab
Created a excel spreadsheet to calculate expected values
Gather the necessary materials to build the circuit
Built the circuit and measured the inductors in a series circuit
Recorded the data on the lab sheet
Built the circuit and measured the inductors in a parallel circuit
Recorded the data on the lab sheet

## Slide 70: Lab 12 – Series/Parallel Inductors

## Slide 71: Lab 12 – Series/Parallel Inductors
Series |  | 
L1= | 1 | mH
L2= | 2.2 | mH
L3= | 4.7 | mH
LT= | 7.9 | mH

## Slide 72: Lab 12 – Series/Parallel Inductors
Parallel |  | 
L1= | 1 | mH
L2= | 2.2 | mH
L3= | 4.7 | mH
LT= | 599.8E-3 | mH

## Slide 73
Summary
  This lab was pretty straight forward since measuring resistors is very basic by now. Inductors are measured and calculated the exact same way resistors are.
Lab 12 – Series/Parallel Inductors

## Slide 74: Lab 13 – RL Lab

## Slide 75: Lab 13 – RL Lab
Objective
  The objective of this lab was to measure and record the value of specific inductors using the LCR meter. After that we are to change the frequency and observe how it impacts the voltage.
Equipment and Material
  Jumper wires, Digital Multimeter, breadboard, Function Generator, LCR meter, Inductors: 1 mH, 2.2 mH, 4.7 mH, Resistors: 100 ohm.

## Slide 76: Lab 13 – RL Lab
Procedure
Created a multisim circuit to simulate the lab
Gather the necessary materials to build the circuit
Built the circuit and measured the inductance of each inductor when they were implemented into the circuit
Recorded the data on the lab sheet
Had partner change the frequency while I recorded the output voltage on the lab sheet
Put the results in excel and created a graph that relates input voltage to output voltage

## Slide 77: Lab 13 – RL Lab

## Slide 78: Lab 13 – RL Lab

## Slide 79: Lab 13 – RL Lab

## Slide 80
Summary
  In this lab we measured the true value of the inductors using the LCR meter and the true value of the resistor using the millimeter. We were able to use multisim to simulate the different frequencies for each inductor.
Lab 12 – Series/Parallel Inductors

## Slide 81: Other Work

## Slide 82: Other Work
AC Excel Spreadsheet

## Slide 83: Other Work
Lecture 2 Simulation

## Slide 84: Other Work
Lecture 2 Slide 31

## Slide 85: Other Work
Lecture 3 Slide 7

## Slide 86: Other Work
Lecture 4 Slide 4

## Slide 87: Other Work
Lecture 4 Slide 4

## Slide 88: Other Work
Lecture 5 Slide 6
Va = | 9 | V
R1 = | 470 | Ω
R2 = | 1000 | Ω
R3 = | 2200 | Ω
IT=RT/Va | IT = | 32.2E-3 | A
I1=Va/R1 | I1 = | 19.1E-3 | A
I2=Va/R2 | I2 = | 9.0E-3 | A
I3=Va/R3 | I3 = | 4.1E-3 | A
RT=1((1/R1)+(1/R2)+(1/R3)) | RT = | 279.2E+0 | Ω

## Slide 89: Other Work
Lecture 5 Slide 14

## Slide 90: Other Work
Lecture 6 Slide 11
 | Circuit 1 | 
R1 = | 10.0E+3 | Ω
R2 = | 10.0E+3 | Ω
R3 = | 10.0E+3 | Ω
R4 = | 10.0E+3 | Ω
R5 = | 10.0E+3 | Ω
R6 = | 10.0E+3 | Ω
Rt = | 17.1E+3 | Ω
 | Circuit 2 | 
R1 = | 10.0E+3 | Ω
R2 = | 10.0E+3 | Ω
R3 = | 5.0E+3 | Ω
R4 = | 10.0E+3 | Ω
R5 = | 10.0E+3 | Ω
Rt = | 17.1E+3 | Ω
 | Circuit 3 | 
R1 = | 10.0E+3 | Ω
R2 = | 10.0E+3 | Ω
R3 = | 25.0E+3 | Ω
Rt = | 17.1E+3 | Ω
 | Circuit 4 | 
R1 = | 10.0E+3 | Ω
R2 = | 7.1E+3 | Ω
Rt = | 17.1E+3 | Ω

## Slide 91: Other Work
Lecture 6 Slide 11b

## Slide 92: Other Work
Lecture 11 Slide 18

## Slide 93: Other Work
Lecture 11 Slide 20

## Slide 94: Other Work
Lecture 14 Slide 5

## Slide 95: Other Work
Lecture 14 Slide 5a

## Slide 96: Other Work
Multisim Current

## Slide 97: Other Work
Ohms

## Slide 98: Other Work
Week 7 First Circuit

## Slide 99: Other Work
Week 12

## Slide 100: Other Work
Week 12

## Slide 101: Other Work
Week 12a

## Slide 102: Other Work
Week 12b

## Slide 103: Other Work
Week 13xc

## Slide 104: Other Work
Week 13xL

## Slide 105: Other Work
Week 13