## Slide 1: EECT 101-50C Lab Notebook
ELECTRONIC PROJECTS
Fall 2015
Olivia Koehler
12-16-15

## Slide 2: Table of Contents
Lab 1 – Test Equipment and Resistors 3
Lab 2 – Resistors and Ohm’s Law 10
Lab 3 – Resistors and Multisim 18
Lab 4 – Test Equipment Basics 28
Lab 5 – Capacitors, Inductors 37
Lab 6 – Learn to Solder 45
Lab 7 – Component Identification/First Solder Kit 50
Lab 8 – 555 Timer Chip 57
Lab 9 – Filters 65
Lab 10 – Square Wave to Sine Wave 72
Lab 11 – Troubleshoot Home Electronics/Test TTL Chips 77
Lab 12 – Lissajous Pattern 83
Lab 13 – AC to DC Power Supplies 90
Lab 14 – ESD Precautions/Test LEDs 99
Lab 15 – Plan/Prepare/Test Solder Kit 108
Lab 16 – Final Solder Kit 114

## Slide 3: Lab 1 – Test Equipment & Resistors

## Slide 4: Lab 1 – Test Equipment & Resistors
Objective
    1. To understand what a resistor is.
    2. To learn the purpose of color codes.
Equipment and Material
    MultiMeter: Gw Instek GDM-8245 SN: CL860260
    Handheld Meter: OTE INSTRUMENTS SN: DT-6830

## Slide 5: Lab 1 – Test Equipment & Resistors
Research and Information
  http://www.allaboutcircuits.com/textbook/reference/chpt-2/resistor-color-codes/ - (Value of Red Band Tolerance.)
  https://www.youtube.com/watch?v=kvQBhXo_tF0 – (Resistor Color Codes.)
  https://www.youtube.com/watch?v=HrZZMhWZiFk – (Resistors.)

## Slide 6: Lab 1 – Test Equipment & Resistors
Procedure
Received three resistors with varying values; R1, R2, and R3.
Following the color code rules, I determined the approximate value of each resistor.
Using a Multimeter, I measured the resistance values of all resistors.
Using Excel, I was able to find whether or not the resistors were within their tolerance ranges;
with the true or false equation.

## Slide 7: Lab 1 – Test Equipment & Resistors
Excel

## Slide 8: Lab 1 – Test Equipment & Resistors
  Pictures
Testing
Resistor

## Slide 9: Lab 1 - Test Equipment & Resistors
  Conclusion
  - I learned how the resistor color-code system works, and how to calculate their values.
  - Everything worked just fine, the only issue found was a resistor which was below the nominal.

## Slide 10: Lab 2 – Resistors and Ohm’s Law

## Slide 11: Lab 2 – Resistors and Ohm’s Law
Objective
    1. To understand how resistors work in Series and Parallel
    2. To learn how to use a Multimeter to measure V,I and R on a bread board.
Equipment and Material
    5 different resistors
    MultiMeter: Gw Instek GDM-8245 SN: CL860260
    DC Power Supply: RSR HY1502D SN: 022510041

## Slide 12: Lab 2- Resistors and Ohm’s Law
Research and Information
  https://www.youtube.com/watch?v=d34-VKc2cyY - (Ohm's Law, The Basics.)
  https://www.youtube.com/watch?v=KK5pxJxxyA0 – (Series Circuit Analysis part 1.)
  https://www.youtube.com/watch?v=s9vpe5a9LIE – (Series Circuit Analysis part 2.)
https://www.youtube.com/watch?v=ruRnqmQ5HIE – (Series Circuit Analysis part 3.)
https://www.youtube.com/watch?v=pZSI0O2naLY - (Analyzing a Series-Parallel Circuit.)
https://www.youtube.com/watch?v=qJZCHExi4Pk – (Ohm's Law Calculations for Simple Circuits.)

## Slide 13: Lab 2 – Resistors and Ohm’s Law
Procedure
Received five resistors with varying values. Using various combinations, placed them in a bread bored and measured IT, VT and RT.
The two types of circuits made were series and parallel. Each set was made up of first three resistors and then five.
For each set I measured IT and RT with the aid of a multimeter. Only for series did I measure the voltage points for each resistor. (This was because voltage is the same throughout a parallel circuit.)
Using Excel, I proved using ohms law that the measurements taken in the real world were accurate.

## Slide 14: Lab 2 – Resistors and Ohm’s Law
Excel

## Slide 15: Lab 2 – Resistors and Ohm’s Law
Pictures

## Slide 16: Lab 2 – Resistors and Ohm’s Law
Pictures

## Slide 17: Lab 2 – Resistors and Ohm’s Law
Conclusion
  - I learned how current, resistance and voltage all relate to one another in a circuit.
  - The only issue had, was one misplaced wire. Once the problem was resolved everything ran accordingly.
  - If I had to practice any one thing, it would be making sure my wires are lined up with the correct columns.

## Slide 18: Lab 3 – Resistors and Multisim

## Slide 19: Lab 3 – Resistors and Multisim
Objective
    1. To become familiar with Multisim.
    2. To learn how to calculate equivalent resistance for both series and parallel circuits.
    Equipment and Material
    Multisim

## Slide 20: Lab 3 – Resistors and Multisim
Research and Information
  https://www.youtube.com/watch?v=10Rt2p3seV4 - (MultiSim 101.)
  https://www.youtube.com/watch?v=2UQPd0pj6uc– (MultiSim 102.)
  https://www.youtube.com/watch?v=3G5V0Hxjkbg– (Measure R with an ohmmeter.)
https://www.youtube.com/watch?v=8P4oFw6sIzQ– (Measure DC V with a voltmeter indicator.)
https://www.youtube.com/watch?v=8h2SAZ9gkBA - (Measure DC I with an ammeter indicator.)

## Slide 21: Lab 3 – Resistors and Multisim
Procedure
Learn and understand all of the different ways Multisim can be utilized.
Using the same value of resistors from the previous lab, create multiple circuits.
Take readings from each circuit made recording V, R, and I.
Compare the result from multisim to the results received from Lab 2.

## Slide 22: Lab 3 – Resistors and Multisim
Multisim
Series R1, R2, R3
IT
RT
V123

## Slide 23: Lab 3 – Resistors and Multisim
Multisim
Series R1, R2, R3, R4, R5
IT
RT

## Slide 24: Lab 3 – Resistors and Multisim
Multisim
Series R1, R2, R3, R4, R5
V12345

## Slide 25: Lab 3 – Resistors and Multisim
Multisim
Parallel R1, R2, R3
IT
RT

## Slide 26: Lab 3 – Resistors and Multisim
Multisim
Parallel R1, R2, R3, R4, R5
IT
RT

## Slide 27: Lab 3 – Resistors and Multisim
Conclusion
  I learned how there are many different ways to do one thing in Multisim. Some being easier to use then others. I also learned that I can use Multisim to check my circuits created in the “real world”.
  - I had no issues using Multisim.

## Slide 28: Lab 4 – Test Equipment Basics

## Slide 29: Lab 4 – Test Equipment Basics
Objective
    1. To understand how to use an oscilloscope and function generator.
    2. To learn how to take proper readings from an oscilloscope in conjunction with a function generator.
Equipment and Material
    Oscilloscope: Tektronix TDS-220 SN: B083238
    Function Generator: Gw Instek GFG-8210 SN: C705255

## Slide 30: Lab 4 – Test Equipment Basics
Research and Information
  https://www.youtube.com/watch?v=dBVWv7enDsU- (Use of Basic Laboratory Equipment
  0-Scope.)
  https://www.youtube.com/watch?v=Zink6v6TXk4– (Use of Basic Laboratory Equipment
  F-Generator.)
  https://www.youtube.com/watch?v=dTPHSDoWKU0– (Test Equipment- The O-Scope.)
https://www.youtube.com/watch?v=7nwIIPN9QEY– (Tektronix Tutorial Part 1.)
https://www.youtube.com/watch?v=8VEg6L2QG5o- (AC vs DC Explained.)
https://www.youtube.com/watch?v=OFGm-Pel4Hg– (Triggering controls and their usage.)

## Slide 31: Lab 4 – Test Equipment Basics
Procedure
A function generator and an oscilloscope were hooked together.
Following the directions given, changed the settings on the function generator and observed the readings from the oscilloscope.
As the readings would change and/or needed to be adjusted to meet the parameters of the experiment, the readings were recorded.

## Slide 32: Lab 4 – Test Equipment Basics
Excel

## Slide 33: Lab 4 – Test Equipment Basics
Excel

## Slide 34: Lab 4 – Test Equipment Basics
Pictures

## Slide 35: Lab 4 – Test Equipment Basics
Conclusion
  I learned how the different controls on a function generator effect the outcome of what appears on the oscilloscope screen. Also, I learned how to use the cursors on the oscilloscope to take readings from the screen.
  - I did have trouble adjusting the function generator to get the readings I needed from the oscilloscope, however with much practice I feel more comfortable with the unit.

## Slide 36: Lab 5 – Capacitors, Inductors

## Slide 37: Lab 5 – Capacitors, Inductors
Objective
    To under stand LCR meter and how to measure inductors and capacitors including custom hand-wound inductors.
    To learn how to run and LCR meter, and take readings from one.
Equipment and Material
    4 Capacitors: 4.7pF, 0.0033uF, 0.01uF, and electrolytic 4.7uF
    3 Inductors: 100uH, 22mH, and 100mH
    3 Custom Wound Inductors: T68 core w/ 10 turn, T68 core w/ 15 turns, and T80 core w/ 20 turns
    LCR Meter: LCR-819 SN:GEN220267
    Bench 1- Caliper

## Slide 38: Lab 5 – Capacitors, Inductors
Research and Information
  https://www.youtube.com/watch?v=X707xxqB1Qc - (What is a Capacitor? P1.)
  https://www.youtube.com/watch?v=gOwJLgjRtw8 – (What is a Capacitor? P2.)
  https://www.youtube.com/watch?v=t9Qwx75eg8w– (How a Capacitor Works.)
https://www.youtube.com/watch?v=WKFnuHfmx00– (What is an Inductor? P1.)
https://www.youtube.com/watch?v=rqvqIQSBZc8 - (What is an Inductor? P2.)
https://www.youtube.com/watch?v=NgwXkUt3XxQ – (Inductor basics.)

## Slide 39: Lab 5 – Capacitors, Inductors
Procedure
Using and LCR meter measure the values of 4 different caps and 3 different inductors.
Hand wound 3 different inductors using 28AWG magnet wire, and calculated possible values using excel.
Measured the hand wound inductors, and compared them to excel equations.

## Slide 40: Lab 5 – Capacitors, Inductors
Pictures
Capacitor

## Slide 41: Lab 5 – Capacitors, Inductors
Pictures
Inductor

## Slide 42: Lab 5 – Capacitors, Inductors
Pictures
H
A
N
D
W
O
U
N
D

## Slide 43: Lab 5 – Capacitors, Inductors
Conclusion
  I learned how to calculate an inductors value using its permeability.
  - I did have some trouble with the equation, however it was a simple solution to an easy mistake.

## Slide 44: Lab 6 – Learn to Solder

## Slide 45: Lab 6 – Learn to Solder
Objective
Practice soldering components to a board.
Equipment and Material
Soldering Machine: (WES51)

## Slide 46: Lab 6 – Learn to Solder
Research and Information
https://www.youtube.com/watch?v=vIT4ra6Mo0s - Solder & Flux
https://www.youtube.com/watch?v=Q9G9gaokqvM - Joining Stranded Wires
https://www.youtube.com/watch?v=oqV2xU1fee8 - How to Solder
https://www.youtube.com/watch?v=-lnRf2biz50 -Removing solder
https://www.youtube.com/watch?v=j1ZnkTC5bps - How to tin a soldering iron tip
https://www.youtube.com/watch?v=BxeDkcAa4Fs - The Basics

## Slide 47: Lab 6 – Learn to Solder
Procedure
Using twelve different components, we identified each one.
After identifying the components, each one was soldered to the board.

## Slide 48: Lab 6 – Learn to Solder
Pictures
Resistors
Capacitors
Diode
VaResistor
Semiconductor
Capacitor

## Slide 49: Lab 6 – Learn to Solder
Conclusion
  I learned how to solder components to a board.
  - I also learned how to use data sheets to identify components which may be unknown.

## Slide 50: Lab 7 -Component Identification & Solder Kit

## Slide 51: Lab 7 -Component Identification & Solder Kit
Objective
- To identify all the different components given in a soldering kit.
- On a CD-1 board, one must identify the two families of ICs used and what the various suffixes mean.
Equipment used
Solder Machine: (WES51)

## Slide 52: Lab 7 -Component Identification & Solder Kit
Research and Information
http://www.howtogeek.com/63630/how-to-use-a-soldering-iron-a-beginners-guide/ (Beginning solder)
https://mightyohm.com/files/soldercomic/FullSolderComic_EN.pdf (solder is easy)
http://www.build-electronic-circuits.com/how-to-solder/ (How to solder)

## Slide 53: Lab 7 -Component Identification & Solder Kit
Procedure
1. Document the quantity of each type of component. On the CD-1 board, identify the two families of ICs used and what the various suffixes mean.
2. Evaluate the impact of removing middle breadboard screws and how to lower 4 corner countersunk screws flush to the top for placement of new breadboard on top using strong adhesive tape.

## Slide 54: Lab 7 -Component Identification & Solder Kit
Pictures
Electrolytic Capacitor
Disc Capacitor
Diode
Semiconductor
IC
Resistor

## Slide 55: Lab 7 -Component Identification & Solder Kit
Pictures

## Slide 56: Lab 7 -Component Identification & Solder Kit
Conclusion
- All of the components were identified and soldered to the board.
- Even though I am still new to soldering I have come a long way sense my first time soldering.

## Slide 57: Lab 8- 555 Timer Chip

## Slide 58: Lab 8- 555 Timer Chip
Objective
- To research the 555 Timer chip, and breadboard two types of LEDs creating a typical flashing circuit for the following values: 0.5Hz, 1Hz, 4Hz.
Equipment used
Oscilloscope: TDS-220 SN:B083238
DC Power Supply: HY1802D SN:022510041

## Slide 59: Lab 8- 555 Timer Chip
Research and Information
https://en.wikipedia.org/wiki/555_timer_IC (Info on timer)
http://www.electronics.dit.ie/staff/mtully/555%20folder/555%20timer.htm (the 555 timer)

## Slide 60: Lab 8- 555 Timer Chip
Procedures
1. Find formula online to set frequency and use Excel to calculate values needed for the 3 frequencies.
2. Use an oscilloscope to verify all 3 frequencies by calculating the frequency from the period.
3. Record all measurements on worksheet and answer all questions.

## Slide 61: Lab 8- 555 Timer Chip
Work Sheet

## Slide 62: Lab 8- 555 Timer Chip
Work Sheet

## Slide 63: Lab 8- 555 Timer Chip
Pictures

## Slide 64: Lab 8- 555 Timer Chip
Summary
Hooking up the circuit was fairly simple, especially after looking up the 555 timer data sheet. I am still getting used to operating the oscilloscope, however getting the readings I needed came pretty easily.

## Slide 65: Lab 9- Filters

## Slide 66: Lab 9- Filters
Objective
- To research RC electronic filters.
To build an RC low pass filter and measure the frequency response from 10 Hz to 100,000 Hz.
Also, to plot Vout vs. Freq in Excel and find the cutoff frequency fc and indicate on the plot using a text box and arrow.
Equipment used
Oscilloscope: (TDS-220 SN:B083238)
LCR Meter: (LCR-819 SN:GEN220267)
Multimeter: (GDM-8245 SN:CL860260)

## Slide 67: Lab 9- Filters
Research and Information
http://www.niu.edu/~mfortner/labelec/lect/p575_07a.pdf (Filters Circuits)
http://www.dummies.com/how-to/content/making-lowpass-and-highpass-filters-with-rc-circui.html (Low Pass & High Pass)

## Slide 68: Lab 9- Filters
Procedures
Build an RC low pass filter.
Measure the frequency response from 10 Hz to 100,000 Hz.

## Slide 69: Lab 9- Filters
Pictures

## Slide 70: Lab 9- Filters
Summary
I learned how to properly hook up an RC circuit, and how to properly hook up all of the wires.

## Slide 71: Lab 10 - Square Wave to Sine Wave

## Slide 72: Lab 10 - Square Wave to Sine Wave
Objective
1. Research a way to convert a square wave to a sine wave using only resistors and capacitors (R and C), then build and demonstrate in the lab.
2.To get an output signal that looks close in shape to a sine wave with at least a 500mVp-p amplitude.
Equipment used
Oscilloscope: (TDS-220 SN:B083238)
Function Generator: (GFG-8210 SN:C705255)
DC Power Supply: (HY1802D SN:022510041)

## Slide 73: Lab 10 - Square Wave to Sine Wave
Research and Information
http://www.ti.com/lit/an/sbfa003/sbfa003.pdf (Square to Sine)
http://www.instructables.com/answers/turn-a-square-wave-froma-555-into-a-sine-wave/ (Instructorless)
http://forum.allaboutcircuits.com/threads/square-wave-to-sine-wave-conversion.32396/ (All about circuits)

## Slide 74: Lab 10 - Square Wave to Sine Wave
Procedure
Use a function generator for the input and set it for a square wave at 100 Hz and 5V amplitude with a 50% duty cycle.
Use an oscilloscope to display the input square wave on Channel 1 and the output sine wave on Channel 2.
The square wave should show little or no degradation when displayed on the scope, i.e. no curving or rounding on the top or bottom.

## Slide 75: Lab 10 - Square Wave to Sine Wave
Pictures

## Slide 76: Lab 10 - Square Wave to Sine Wave
Summary
I learned how to change a square wav into a sign wave with the aid of capacitors. Not an easy task, especially looking for help online, however the circuit was success.

## Slide 77: Lab 11 – Troubleshoot Home Electronics

## Slide 78: Lab 11 – Troubleshoot Home Electronics
Objective
- Breadboard a test circuit to test one chip at a time using 74LS series TTL chips from parts bin.
- Troubleshoot and fix home electronics.
Equipment used
Digital Multimeter: (GDM-8245 SN: CL860260)

## Slide 79: Lab 11 – Troubleshoot Home Electronics
Research and Information
https://www.facstaff.bucknell.edu/mastascu/eLessonsHTML/Labs/Logic/LabLogic1A.html (Logic Lab)
http://www.instructables.com/id/FAN-repair/ (Fan Repair)

## Slide 80: Lab 11 – Troubleshoot Home Electronics
Procedures
Open Fan and test motor using a multi meter.
Check when fan is running, does it over heat? Does it make any noise?
Test axel to make sure it still works.
Come up with a solution to the problem.

## Slide 81: Lab 11 – Troubleshoot Home Electronics
Pictures
Home
Electronic
IC Test
Circuit

## Slide 82: Lab 11 – Troubleshoot Home Electronics
Summary
I took the fan apart and had to clean it because it was very dusty. The problem to begin was, was that the fan didn’t work what so ever.
Cleaning it did not change anything, and after testing the switch, we found the switch still worked.
The fan continued to make weird noises, after doing many tests it was time to wait and continue the next week.

## Slide 83: Lab 12-Lissajous Pattern/Misc Troubleshooting/Test TTL Chips

## Slide 84: Lab 12-Lissajous Pattern/Misc Troubleshooting/Test TTL Chips
Objective
1. Research a way to display a circle or ellipse on an oscilloscope.
2. Test circuit to test one chip at a time using 74LS00 series TTL chips.
3. Troubleshoot and fix home electronics.
Equipment Used
Oscilloscope: (TDS-220 SN: B083238)
Function Generator: (GFG-8210 SN:C705255)
Digital Multimeter: (GDM-8245 SN: CL860260)

## Slide 85: Lab 12-Lissajous Pattern/Misc Troubleshooting/Test TTL Chips
My research Information
http://www.ivytechengineering.com/stores/74ls/files/74ls02.pdf (DATA Sheet)
https://www.picotech.com/library/oscilloscopes/xy-display-mode (XY Display Mode)
http://mathworld.wolfram.com/LissajousCurve.html (Lissajous Curve)

## Slide 86: Lab 12-Lissajous Pattern/Misc Troubleshooting/Test TTL Chips
Procedures
Demonstrate a way to display a circle on an oscilloscope, using reference material.
Breadboard a test circuit to test one chip at a time using 74LS00 series TTL chips from untested parts bin
Troubleshoot and fix home electronics.

## Slide 87: Lab 12-Lissajous Pattern/Misc Troubleshooting/Test TTL Chips
Pictures

## Slide 88: Lab 12-Lissajous Pattern/Misc Troubleshooting/Test TTL Chips
Pictures

## Slide 89: Lab 12-Lissajous Pattern/Misc Troubleshooting/Test TTL Chips
Summary
Using the Oscilloscope a circle was created on the main screen. It was difficult at first because, continuing to make a diagonal line. After many attempts, and a lot of frustration a circle was finally made.
Another circuit was created to test IC’s there were no issues.
With more work on the fan it was decided to us WD40 on the axel to see if that will help with the fans rotations.

## Slide 90: Lab 13 - AC to DC Power Supplies

## Slide 91: Lab 13 - AC to DC Power Supplies
Objective
Research how AC is converted to DC for a low voltage power supply.
Equipment Used
Oscilloscope: (TDS-220 SN:B083238)
Digital Multimeter: (GDM-8245 SN: CL860260)

## Slide 92: Lab 13 - AC to DC Power Supplies
My Research
http://www.cableorganizer.com/articles/ac-power.htm (Difference between AC to DC)
https://learn.sparkfun.com/tutorials/alternating-current-ac-vs-direct-current-dc (Info on alternating current)

## Slide 93: Lab 13 - AC to DC Power Supplies
Procedures
Use a function generator as a secondary output of the transformer, by using a sine wave at 60 Hz.
Set the function generator amplitude so that it provides 5VDC at the output of my power supply.
Show on the oscilloscope the sine wave on channel 1, and the 5VDC output on channel 2. Took pictures of breadboard, scope, function generator.

## Slide 94: Lab 13 - AC to DC Power Supplies/Misc Troubleshooting
Question: Why does the sine wave amplitude have to be higher than 5V?
Answer: Because the actual DC equivalent value of the sine wave is 0.707 x peak value. So in order to get five vaults doc equivalent the peak must be 7.07 volts. This is because it is constantly changing over time, and is never the same value at different points on time.

## Slide 95: Lab 13 - AC to DC Power Supplies
Pictures
AC to DC
Sine Wave

## Slide 96: Lab 13 - AC to DC Power Supplies
30 yr. old
Custom Supply
Test

## Slide 97: Lab 13 - AC to DC Power Supplies
Home
Electronic

## Slide 98: Lab 13 - AC to DC Power Supplies
Summary
Ac to DC was hooked up to an oscilloscope. Some difficulties were found at first, but the right readings were eventually found. After understanding the controls.
Fan from previous week worked with the aid of WD40.
CD shuffler was extremely dirty and needed to be cleaned out, was hooked to an oscilloscope to see if it could still read music. The results were that it could.

## Slide 99
Lab 14 - ESD Precautions/Test LEDs

## Slide 100: Lab 14 - ESD Precautions/Test LEDs
Objective
Research ESD (electro-static discharge) and how it can affect electronic devices.
Test/sort 6 types of 200 total LEDs and separate flashing from non-flashing.
Equipment used
Power Supply: (HY1802D SN:02510041)

## Slide 101: Lab 14 - ESD Precautions/Test LEDs
Research and Information
http://ecmweb.com/content/electrostatic-discharge-causes-effects-and-solutions (Info on ESD)
http://www.aes.org/aeshc/docs/3mtape/soundtalk/soundtalkbull22.pdf (Magnetic Properties of Tape)

## Slide 102: Lab 14 - ESD Precautions/Test LEDs
Procedures
Find some of the ways to prevent or minimize ESD for safe handling.
Understand what types of house hold items generate voltage.
Build a circuit to test different types of LEDs.

## Slide 103: Lab 14 - ESD Precautions/Test LEDs
Pictures

## Slide 104: Lab 10 - Square Wave to Sine Wave
Pictures
LED Testing

## Slide 105: Lab 14 - ESD Precautions/Test LEDs
Pictures
Chip Testing

## Slide 106: Lab 14 - ESD Precautions/Test LEDs Troubleshooting

## Slide 107: Lab 10 - Square Wave to Sine Wave
Summary
I was able to learn about ESD, why it occurs and how to prevent it from occurring. Although it can not be completely illuminated from a site, it is possible take precautionary steps.
The circuit created to test the LEDs worked well, almost all of the LEDs were good.
We found out that Charlie browns batteries were bad to begin with.

## Slide 108: Lab 15- Plan, Prepare, Test Solder Kit

## Slide 109: Lab 15- Plan, Prepare, Test Solder Kit
Objective
Create an outline/plan for your solder kit next week.
Equipment Used
DC Power Supply: (HY1802D SN:022510041)

## Slide 110: Lab 15- Plan, Prepare, Test Solder Kit
Research and Information
http://www.instructables.com/id/How-to-solder/ (Soldering)
https://mightyohm.com/files/soldercomic/FullSolderComic_EN.pdf (Soldering made easy)

## Slide 111: Lab 15- Plan, Prepare, Test Solder Kit
Procedures
1. step by step to prepare and assemble your kit including testing individual parts before assembly and possible ways to protect against overheating
2. include some steps you would take to troubleshoot your kit if it doesn't work including a) what to check if doesn't power up; b) what to check if partially operational

## Slide 112: Lab 15- Plan, Prepare, Test Solder Kit
Pictures of Plan

## Slide 113: Lab 15- Plan, Prepare, Test Solder Kit
Summary
The kit I selected was the Brain Game kit. I went through all of the parts and made sure everything was present and accounted for. I made a strategy to help me make sure that I will be able to properly complete my final test.
Also, I brushed up on soldering by reading and watching soldering tutorials.

## Slide 114: Lab 16- Final Solder Kit

## Slide 115: Lab 16- Final Solder Kit
Objective
To build/solder final kits
Equipment Used
DC Power Supply: (HY1802D SN:022510041)
Digital Multimeter: (GDM-8245 SN: CL860260)
LCR Meter: (LCR-819 SN:GEN220267)

## Slide 116: Lab 16- Final Solder Kit
Research and Information
http://www.instructables.com/id/Soldering-tips-and-tricks/ (Soldering Tips)
http://www.aaroncake.net/electronics/solder.htm (Soldering Tutorial)

## Slide 117: Lab 16- Final Solder Kit
Procedures
Test all pieces to make sure all are properly functioning.
Solder parts following the recommended order on the directions.
Take time to make sure each metal pad and wire is coated with the solder (but not too much!)
Test the device to make sure it works.

## Slide 118: Lab 16- Final Solder Kit
Schematic

## Slide 119: Lab 16- Final Solder Kit
Pictures - Materials
Led
Diode
Diode
Resistor
Transistor
Capacitor
IC
Switch
LS

## Slide 120: Lab 16- Final Solder Kit
Pictures – Testing Materials
Transistor
Resistor

## Slide 121: Lab 16- Final Solder Kit
Pictures – Testing Materials
Capacitor
LED Test
Circuit

## Slide 122: Lab 16- Final Solder Kit
Pictures – Testing Materials
Diodes

## Slide 123: Lab 16- Final Solder Kit
Pictures – Finished Product

## Slide 124: Lab 16- Final Solder Kit
Video

## Slide 125: Lab 16- Final Solder Kit
Summary
Everything worked out wonderfully, I have definitely come a long way with soldering. Nothing was touching, and everything was properly covered (only a few had a bit too much).
I really enjoyed this class this semester, it was a lot of fun, and I learned so much!
